## Slide 1: WF on UE RF requirements for 3.3-3.8 GHz, 3.3-4.2 GHz and 4.4-5 GHz
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 NR#84 Meeting
Berlin, Germany, 21st – 25th August, 2017
R4-1708971

## Slide 2: Background
UE RF requirements for below bands are being discussed to complete them by December 2017
  Band n77: 3.3-4.2 GHz
  Band n78: 3.3-3.8 GHz
  Band n79: 4.4-5.0 GHz

## Slide 3: WF on Band n77 and n78
2CC Intra-band contiguous CA of aggregated CBW
  120, 140, 150, 160, 180 and 200 MHz
MOP
  23 dBm +2/-3 dB for Band n77 and n78 of PC3
Additional spur requirements for async operations
  Not to be specified at least in Rel-15
DTib and DRib (for CA/DC combo including Band n77 or n78)
  To discuss if values of LTE CA including B42 can be improved considering more filter data and/or possible UE architectures (if any)
Protected bands
  To specify bands for Japan, Europe, Korea and China at least
  Specific protected bands to be provided in the next meeting
REFSENS
  Filter data was provided in [1] for Band n77 and n78 as shown in annex
  On top of that, to study LNA aspects for both bands including further filter data whose attenuation is at least typ. 35 dB for < 2.69 GHz
    Insertion loss for the 3.3-3.8GHz needs to be included in the filter data
    Achievable/required attenuation at 5.15-5.925 GHz is FFS
Out-of-band blocking
  To study applicability of other filter technologies other than LTCC based on simulation and/or measurement input in the next meeting
Other
  Features such as HPUE, 2Tx to be specified for Band n78 will also be introduced in Band n77 in Rel-15

## Slide 4: WF on Band n79
2CC Intra-band contiguous CA of aggregated CBW
  120, 140, 150, 160, 180 and 200 MHz
MOP and REFSENS
  To confirm if Band n79 UEs need to protect 5.15-5.925 GHz first
  In parallel, to study performance of PA, LNA and other RF components including filter data
    Insertion loss for the 4.8-5GHz range needs to be included in the filter data
    Achievable/required attenuation at 5.15-5.925 GHz is FFS
DTib and DRib (for CA/DC combo including Band n79)
  To study if separate antenna architecture can be assumed
Protected bands
  To specify bands for Japan and China at least
  Specific protected bands to be provided in the next meeting
Out-of-band blocking
  To evaluate applicability of other filter technologies other than LTCC based on simulation and/or measurement data in the next meeting
  *Blue parts are “delta” compared to previous slide for Band n77 and n78

## Slide 5: Reference
[1] R4-1707507_UE RF requirements for 3.3-3.8 GHz and 3.3-4.2 GHz, NTT DOCOMO, INC.
[2] R4-1707508_UE RF requirements for 4.4-4.99 GHz, NTT DOCOMO, INC.
Parameter | Frequency range | Vendor 1 |  | Vendor 2 |  | Vendor 3 | 
 |  | Band n78 BPF | Band n77 BPF | Band n78 BPF | Band n77 BPF | Band n78 BPF | Band n77 BPF
Insertion loss (ETC) | 3300-3400 MHz | 1.1 dB | 1.1 dB | 2.0 dB | 2.0 dB | 1.9 dB | 1.9 dB
 | 3400-3800 MHz | 0.95 dB | 0.95 dB | 1.5 dB | 1.5 dB |  | 
 | 3800-4200 MHz | - | 1.2 dB | - |  | - | 
Attenuation (Typ) | 698-2690 MHz | 35 dB | 39.8 dB | 45 dB | 45 dB | 51.8 dB | 50.5 dB
 | 5150-5925 MHz | 27.8 dB | 31.1 dB | 35 dB | 30 dB | 25 dB | 25.3 dB
Table 2.2-2. Simulation results for Band n77 and n78 in [1]