## Slide 1: WF on RRM/Demod baseline test system
Rohde & Schwarz, Keysight, Anritsu, Spirent, Bluetest
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 - 25, August, 2017
R4-1708996

## Slide 2: Summary of WF document
Demod
  No baseline test system defined
  In this WF the proposal is to highlight additional details of two suitable test system methodologies:
    Test setup with baseband emulation of Multi-AoA
    Test setup with spatial emulation of Multi-AoA
RRM
  Baseline system defined as having a system with at least 1 probe connecting OTA to the DUT
  Requirement of having >1 probe test system is FFS
Questions related to UE requirements have been listed which are to be clarified by RRM/Demod experts

## Slide 3: Demodulation Baseline System: Option A
Test setup with baseband emulation of Multi-AoA:
  Baseband emulation of the channel model
  A positioning system such that the angle between the dual-polarized measurement antenna and the DUT has at least two axes of freedom and maintains a polarization reference
This method needs the following:
  UE antenna pattern known or measured
  Emulate the antenna pattern in the baseband fader
Advantages/Restriction:
  Method can simulate any arbitrary channel models including 38.901
  All possible AoA can be simulated simultaneously
  No restriction to intra-cluster angular spread
  Requirement for beamlock is FFS
  Testability of autonomous UE active beam steering/ tracking aspects of the DUT is difficult

## Slide 4: Demodulation Baseline System: Option B
Test setup with spatial emulation of Multi-AoA:
  System parameters shown below are to be defined based on the inputs from the WF on channel model simplification
  Number of Probes (Can be either movable probes OR static probes with switching)
    Probe location/positioning in Azimuth and Elevation (This parameter will set the limits of effective mapping of the spatial clusters from the channel model)
  Spatial resolution of the probes (Different set of probe resolution(s) can be defined for RRM and Demod test cases)
  Number of active probes (This parameter sets the limit for number of active probes / ports that is needed from the TE)
Advantages/Restriction:
  Allows testability of autonomous UE active beam steering/ tracking aspects of the DUT
  Does not require beam lock
  System is based on the simplification of 38.901 channel models
    The simplification process is done based a reduction process that takes into account the actual spatial charateristics of the channel.
  AoA can be spatially emulated simultaneously, at least one active probe per cluster required
  Spatial probe resolution will determine the accuracy of the PAS (power angular spectrum) for the channel model
  System complexity depends on the number of simultaneous active probes required

## Slide 5: Demodulation Requirements open questions
Since the following assumptions may have impact on the test system complexity, demodulation experts are asked to review the following questions and give possible feedback:
  Do the requirements include scenarios with multiple spatial and delay clusters of the same /multiple beam index?
  Do the requirements include scenarios of mobility for tests such as: active antenna beamsteering capability, baseband tracking of the channel, etc.?
  Do the requirements include the scenarios of any type of 2x2 MIMO implementation (polarization diversity, pattern diversity with same polarization beams) or is it restricted to one approach?

## Slide 6: RRM Baseline System:
From TR(38.810) RRM baseline is = RF baseline with following in addition:
≤2 NR TRxPs emulated
N sets of cross-polarised antennas = Tx from emulated gNB to the DUT
N ≥ NMAX_AoAs = max number of total simultaneously emulated angles of arrival in the chamber
It is FFS how to model propagation conditions between the DUT and the emulated gNB
A positioning system: at least 1 antenna with angular relationship with DUT with two axes of freedom independently controllable (or equivalent functionality)
It is FFS whether more than 1 antenna needs to provide independently controllable angular relationships with DUT.
  Comment: Questions related to the applicability of such system are in the slide 8
Signal transmission in test zone so that signal polarization does not prevent the DUT receiving a consistent, predictable power level  method FFS.
* Bold text is copied from 38.810, text in italics represents comments

## Slide 7: Assumptions for RRM test system
Scenarios required to finalize the RRM Baseline system(s):
  1 NR TRxP scenario  with fading  channel model and test setup from demodulation test can be reused
  2 NR TRxPs scenario with fading  channel model instances need to be defined within RAN4 using the framework of 38.901
  2 NR TRxPs scenario without fading  AWGN applies

## Slide 8: RRM Requirements: Open questions
Since the following assumptions may have impact on the test system complexity, RRM experts are asked to review the following questions and give possible feedback:
  Do the requirements include scenarios with multiple receive AoA of the same beam index from the same cell?
  Do the requirements include scenarios with multiple receive AoA of different beam indices from the same cell?
  Do the requirements include scenarios with multiple receive AoA of beams from different cells?
  Do the requirements include scenarios with any type of 2x2 MIMO implementation (polarization diversity, pattern diversity) or should be limited to polarization diversity?
  Does the UE active beamsteering and tracking capability need to be taken into account in the above scenarios?
  Is a test setup based on static test AoA, with power level change, enough for RRM test cases?
  Can a mapping of the RRM test cases to the criteria listed above be provided?

## Slide 9: Spatial Characteristics: Assumption for RRM requirements
R4-1708552 | Spatial characteristics | Static vs Dynamic
RRC_IDLE State Mobility | Yes | TBD
RRC_INACTIVE state mobility | Yes | TBD
RRC_CONNECTED State Mobility | Yes | TBD
RRC Connection Mobility Control | Re-establishment-Yes Random access-No | TBD
Timing | UE transmit accuracy -Yes UE timer accuracy - FFS | TBD
Signalling characteristics | Yes | TBD
UE Measurements Procedures | Yes | TBD
Measurement Performance Requirements | Yes | TBD
It is requested to confirm/complete the table of assumptions by RRM/Demo experts
More scenarios can be added if/where appropriate

## Slide 10: Way Forward
RRM/Demod experts to review the assumptions/open questions on Demod/RRM requirements and give feedback. (slide 5,7,8,9)
Provide information on further missing aspects for finalizing the baseline setups or/and raise further requirements to the systems
The main purpose should be Rel-15 test coverage.
Requirement to test DUT effectively should drive the definition of baseline system. However the feasibility of testing those requirements needs to be taken into account (cost/timewise).