## Slide 1: Way forward for Rel-14 eCRS-IM WI on network assistant info and UE capability
Ericsson
3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany, 21 - 25 August 2017
R4-1709000

## Slide 2: UE capability for eCRS-IM feature
CRS-IM capability
  UE can indicate per-UE CRS-IM capability if it supports at least one of features on at least one CC in at least one CA configuration
    Rel-14 CRS-IM
    Rel-13 CRS-IM
    Rel-13 DL Control Channel IM (CCIM)
  This capability includes 3 options
    0: full blind detection with the capability to full blindly detect the CRS assistant information without need of CRS assistant information
    1: blind detection of cell id and number of CRS antenna ports without the need of cell id and number of CRS antenna ports in the CRS assistant information. UE needs only MBSFN SF configuration as CRS assistance information
    2: require the full CRS assistant information without blind detection

## Slide 3: WF on UE capability signaling
Capabilities signaling is applied at least for Rel-14 CRS-IM UE
In case RAN2 can support, capabilities signaling defined for Rel-14 can be applied to both Rel-13 and Rel-14 UEs supporting the features
  Rel-14 CRS-IM
  Rel-13 CRS-IM
  Rel-13 DL Control Channel IM (CCIM)
Feasibility of Rel-13 UE capability signaling is subject to RAN2 check

## Slide 4: Optimization of CRS assistant info
There is possibility to improve the CRS assistant information as the following way in order to avoid sending CRS assistant information from network side
  Option 1: Revise the existing signaling as the following to indicate neighboring cells are using the same number of CRS antenna ports and the same MBSFN configuration as the serving cell
    – PresenceAntennaPort1
    – NeighCellConfig
  Option 2: Define new 1 bit flag to indicate that neighbor cells have same configuration as serving cell for the number of CRS ports and/or MBSFN SF configuration
It’s subject to RAN2 to decide the way to optimize the signaling design
Send LS to RAN2 with the above information

## Slide 5: CRS assistance signaling optimization (option 1)
Revise the existing signaling as the following to indicate neighboring cells are using the same number of CRS antenna ports and the same MBSFN configuration as the serving cell
  PresenceAntennaPort1 : revise to indicate exact number of CRS ports in the neighbor cells among {1, 2, 4}
  NeighCellConfig : revise to indicate that MBSFN SF configuration in neighbor cells is same as serving cell so that UE can derive exact MBSFN SF configurations of neighbor cells

## Slide 6: CRS assistance signaling optimization (option 2)
Define new 1 bit flag to indicate that neighbor cells have same configuration as serving cell for the number of CRS ports and/or MBSFN SF configuration
  1 bit flag to indicate that number of CRS ports in neighbor cells is same as serving cell
    UE can assume that all neighboring cells except cells with Rel-13 CRS assistance signaling have same number of CRS ports as serving cell
  1 bit flag to indicate that MBSFN SF configuration in neighbor cells is same as serving cell
    UE can assume that all neighboring cells except cells with Rel-13 CRS assistance signaling have same MBSFN SF configuration as serving cell