## Slide 1: Way forward on SI acquisition time improvement for eFeMTC
Ericsson
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 - 25, August, 2017
R4-1709004

## Slide 2: Background
RAN2 is discussing the SI accumulation across the SI modification window, given by multiplication of DRX cycle (defaultPagingCycle) and coefficient (modificationPeriodCoeff).
However, RAN2 has already confirmed that UE can accumulate SI across the SI window [1]:
  RAN2 confirms that the repetitions SIB1-BR and SIB1-NB can be accumulated using the same SIB1 scheduling information during the modification period associated with each SIB1 (which is 5.12 sec for BL/EC UEs and 40.96 sec for NB-IoT UEs).
  If required, a BL/CE UE can accumulate more repetitions of SIB1-BR during the mod.ification period of SIB1-BR without re-acquiring MIB for schedulingInfoSIB1-BR.
[1] R2-1702324, “LS response to Clarification on SIB1/MIB acquisition delays”, RAN2.

## Slide 3: Way forward
Companies are encouraged to provide the simulation results for SI acquisition time by assuming eFeMTC UE accumulates PDSCH for SI transmission across SIB1-BR/SI window.

## Slide 4: Simulation assumption (SIB1-BR)
Parameters | CE Mode B
System bandwidth | 10MHz
Transmit antennas | 2
Propagation channels | ETU1, EPA1
TBS for SIB1-BR | 208bits
SIB1-BR repetition number within 80ms | 16
SIB1-BR accumulation period (<5120ms) | 80ms, 160ms, 320ms, 640ms
UE receive antennas | 1
UE Frequency offset | 100Hz
Test point (SNR) | -15dB
Evaluation criteria | 99% of SIB1-BR decoding success rate

## Slide 5: Simulation assumption (SIB2-BR)
Parameters | CE Mode B
System bandwidth | 10MHz
Transmit antennas | 2
Propagation channels | ETU1, EPA1
TBS for SIB2-BR | 208bits
si-WindowLength-BR | 40ms
si-RepetitionPattern | everyRF
si-Periodicity | 160ms (rf16)
SIB2-BR accumulation period | 160ms, 320ms, 640ms, 1280ms
UE receive antennas | 1
UE Frequency offset | 100Hz
Test point (SNR) | -15dB
Evaluation criteria | 99% of SIB2-BR decoding success rate