## Slide 1: MIMO OTA TRMS requirements proposal
Intel
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 - 25 August, 2017
Agenda item: 7.2.1.2
Document for: Approval
R4-1709060

## Slide 2: Background
The MIMO OTA requirements framework was approved during the last MIMO OTA Ad-hoc [R4-1706413];
This is the last meeting in MIMO WI extension, the aim is to finalize the requirements for PS1;

## Slide 3: Proposals
Augment the performance requirements definition based on JBPR
The defined TRMS requirement should only be applied for 2x2 MIMO 2rx devices, not for 4rx device although it can be 2x2 capable, due to the difference in the architecture design, measurement method availability and due to the lack of data that can isolate the 4rx UE capability.
Because the B5 and B13 data sets are incomplete, the full picture of the B5/B19 and B13 performance is not available. Therefore, we propose to exclude low bands.
Proposed limit values case are as follows:

## Slide 4: Proposed Limits
Bands and requirement to evaluate [example] |  |  |  |  |  |  | 
Bands |  |  | 3 | 1 | 7 | 41 | 
Include band in JBPF |  |  | x | x | x | x | 
DL Fc |  |  | 1842.5 | 2140 | 2655 | 2593 | 
UL Fc |  |  | 1747.5 | 1950 | 2535 | 2593 | 
Proposed TRMS_70 limits |  |  | -93.0 | -93.0 | -91.0 | -95.5 | 
Proposed TRMS_95 limits |  |  | -91.0 | -91.0 | -89.0 | -93.5 | 
Desired passing rate |  |  | 90% |  |  |  | 
Unacceptable passing rate |  |  | 70% |  |  |  | 
Requirement passing rate |  |  |  |  |  |  | 
 |  |  | B3 pass | B1 pass | B7 pass | B41 pass | All pass
Passing TRMS_70 rate |  |  | 100% | 95% | 95% | 88% | 89%
Passing TRMS_95 rate |  |  | 100% | 95% | 95% | 85% | 88%
Passing TRMS 70&95 rate |  |  | 100% | 95% | 95% | 85% | 88%
Number of DUTs |  |  | 16 | 22 | 22 | 26 | 
Total |  |  |  |  |  |  |