## Slide 1: WF on unwanted spatial emission for NR BS
CMCC
R4-1709080
Agenda : 9.5.2.2
Document for: Approval
3GPP TSG RAN WG4 Meeting #84
Berlin, Germany, 21 - 25 August, 2017

## Slide 2: Background
  In order to guarantee the system performance, some declarations related to unwanted spatial emissions should be included in the scope of RAN4 specifications for 5G NR BS in Rel-15
  A WF on unwanted spatial emissions for NR was approved in R4-1706972 [1], in RAN4#84 meeting( Aug, 2017 ), whether to introduce the unwanted spatial emission declaration will be decided. If the unwanted spatial emission declaration is introduced, one of options related to unwanted spatial emissions should be selected for 5G NR BS in Rel-15
      Option1: SLSR and FBR should be included as declarations for 5G NR BS in Rel-15.
      Option2: Side lobe level and front to back ratio potential requirements can be combined into a “emissions spatial mask” declaration
      Option3: Declared The total power that is radiated outside of the 3dB beamwidth within the context of the NR declarations (assuming similar declarations to AAS with this addition)

## Slide 3: Agreement
  Unwanted spatial emission declaration should be included in the scope of RAN4 specifications for 5G NR BS in Rel-15
Declaration for unwanted spatial emission is shown in slide 4
Unwanted spatial emission declaration should be captured in TS 38.141 and TR 38.xxx(General aspects for RF, RRM and demodulation for NR), which is shown in slide 5
Note: the minimum requirements of unwanted spatial emission can be further considered if a clear benefit is shown

## Slide 4: WF on declaration for Unwanted spatial emission
    Side lobe level and front to back ratio potential requirements can be combined into a “emissions spatial mask” declaration
    Take the below description as a reference for declaration of unwanted spatial emission:
    NOTE: The declaration of unwanted spatial emission may in many circumstances not directly relate to system performance on its own. This is because it is often not possible to differentiate wanted and unwanted radiation, and furthermore because the benefits of optimizing beamforming performance may outweigh the impacts of “unwanted” radiation, leading to systems with apparently higher unwanted radiation also providing superior throughput performance. System performance should additionally be characterized taking all factors into account.
Out of cell directions set | The set of directions that lie outside of the wanted cell
Out of cell power level | the average radiated power outside of the wanted cell
In cell power level | The average radiated power in the wanted cell

## Slide 5: WF on How to capture the declaration of unwanted spatial emission
The declaration of unwanted spatial emission should be capture in TS 38.141 as a optional declaration
The declaration of unwanted spatial emission also should be capture in TR 38.xxx(General aspects for RF, RRM and demodulation for NR)

## Slide 6: References
  [1] R4-1706972 WF on unwanted spatial emissions for NR CMCC
  [2] R4-1707838 Proposal on unwanted spatial emissions for NR BS CMCC
  [3] R4-1707492 Discussion on unwanted spatial emission for NR CATT
  [4] R4-1707963 Discussion on unwanted spatial emission for NR BS ZTE
  [5] R4-1708079 Consideration on Unwanted Spatial Emissions Nokia, Nokia Shanghai Bell
  [6] R4-1708330 Proposal on unwanted spatial emission requirements for NR NEC
  [7] R4-1708111 On declaration of “unwanted” spatial radiation Ericsson
  [8] R4-1708422 Discussion on spatial requirements Huawei