## Slide 1: WF on network-based CRS interference mitigation
Ericsson, Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 Meeting #84 R4-1709102
Berlin, Germany, 21st – 25th August 2017

## Slide 2: General
D2D, V2V, LAA/eLAA: no impact
NB-IoT: FFS
HD-FDD MTC:
  Full BW CRS shall be assumed during UL transmission gaps
  6 RB CRS can be assumed during UL periods regardless of DRX/non-DRX, except for the UL transmission gaps

## Slide 3: RRC_IDLE
Full BW CRS shall be assumed during:
  All configured paging occasions and also [TBD subframes] for warm up & cool down
  SI acquisition (SIB1 and SI-window) and also [TBD subframes] for warm up & cool down
  RA procedure (at least partly), e.g.:
    Prio to RA transmission occasions, [TBD subframes]
    During Msg2 monitoring and also [TBD subframes] for warm up
    During Msg4 monitoring and also [TBD subframes] for warm up
eDRX:
  6 RB CRS may be assumed outside PTW (inside PTW is according to the above)
  FFS additional warm up before the PTW
Investigation on the need for CRS in other idle mode scenarios is not precluded
The above applies also for legacy UE

## Slide 4: RRC_CONNECTED
Non-DRX : full BW CRS in serving cell is provided
  All UE RRM requirements in 36.133 apply
  FeMTC: FFS whether full BW CRS is necesary when UE is not monitoring MPDCCH and not receiving data
DRX is configured: full BW CRS in serving cell during
  UE Active Time and also [TBD subframes] for warm up & cool down
  RA (at least partly)
  on-going retransmissions in UL and DL, in semi-persistently scheduled DL resources, in the resources with HARQ feedback
  SCell activation period and when the SCell is activated except for the SCell deactivation period
  RSTD: existing requirements apply, under full BW CRS in positioning subframes
  Other conditions are not precluded if identified necessary
  Note: Under the above conditions, all existing UE RRM requirements and procedures in 36.133 apply
WB-RSRQ measurement:
  If the UE is configured with widebandRSRQ-Meas to measure WB-RSRQ then the UE shall assume that CRS are available in the measured cell over the AllowedMeasBandwidth (e.g., 50 RBs or larger),
  Otherwise CRS may be transmitted over 6 RBs in neighbor cells (AllowedMeasBandwidth is 6 RBs)
Companies are welcome to provide in RAN4#85 further analysis for legacy UEs, e.g., for
  RLM (e.g., when UE gets out-of-sync and monitors as if in non-DRX)
  need for CRS during SR procedure
  Impact on UL transmit timing requirement
  Deactivated SCells