## Slide 1
WF on SA and NSA UE REFSENS for NR sub-6GHz
Skyworks Solution, Inc. , Nokia, Qualcomm, Ericsson, Sony….
R4-1709141
3GPP TSG-RAN WG4 #84
Berlin, Germany, 21st – 25th August, 2017
Agenda: 9.4.3.1.2

## Slide 2: Background: references
[1] R4-1708175, NR UE REFSENS requirements,
LG Electronics France, RAN4#84
[2] R4-1708444, Sub-6 reference sensitivity,
QUALCOMM CDMA Technologies, RAN4#84
[3] R4-1708494, Guidelines for NR UE REFSENS Requirement for the Different Modes of Operation,
Skyworks Solutions Inc., RAN4#84
In following references NF, IM and SA/NSA assumptions for REFSENS were discussed.

## Slide 3: WF: Procedure for REFSENS calculations for NR sub-6GHz
REFSENS are calculated for SA case per band and channel bandwidths
Separately extra losses related to NSA handling are discussed (common/separate antennas, diplexing, solutions to harmonics/IMD)
This is not reflecting how it will be captured in the spec but the method to share results

## Slide 4: WF: REFSENS for SA per band/Channel BW
REFSENS = -174dBm + NF + 10*log(RXBW) - Diversity gain + SNR + IM
Diversity gain is 3dB for 2 RX antenna case
Antenna correlation issues may be embedded in IM taking into account the frequency range, note that for test the 3dB apply as it is a conducted test.
RXBW is transmission bandwidth per channel BW and SCS. See values in next page
NF is maximum [9-13dB] for C-Bands (n77, n78, n79)
IM is [0.5-2.5dB] for C-Bands (n77, n78, n79)
For bellow 3GHz NF and IM may be different especially taking into account critical FDD cases and could be evaluated per band. Values are FSS
SNR is FSS depending on reference signal and receiver demodulator performance. Assumption is QPSK with coding rate TBD.

## Slide 5: Background: RXBW per Channel BW
Highest RXBW is always for the lowest valid SCS
10*Log (BW) provided in bottom rows
Sub-6GHz | SCS [kHz] | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 100 MHz
SU_CP-OFDM [#RB] | 15 | 25 | 52 | 79 | 106 | 133 | 216 | 270 | NA | NA | NA
 | 30 | 11 | 24 | 38 | 51 | 65 | 106 | 133 | 162 | 217 | 273
 | 60 | NA | 11 | 18 | 24 | 31 | 51 | 65 | 79 | 107 | 135
RXBW [MHz] | 15 | 4.5 | 9.4 | 14.2 | 19.1 | 23.9 | 38.9 | 48.6 | NA | NA | NA
 | 30 | 4 | 8.6 | 13.7 | 18.4 | 23.4 | 38.2 | 47.9 | 58.3 | 78.1 | 98.3
 | 60 | NA | 7.9 | 13 | 17.3 | 22.3 | 36.7 | 46.8 | 56.9 | 77 | 97.2
max RXBW [MHz] |  | 4.5 | 9.4 | 14.2 | 19.1 | 23.9 | 38.9 | 48.6 | 58.3 | 78.1 | 98.3
10*Log RXBW | 15 | 66.5 | 69.7 | 71.5 | 72.8 | 73.8 | 75.9 | 76.9 | NA | NA | NA
 | 30 | 66.0 | 69.4 | 71.4 | 72.6 | 73.7 | 75.8 | 76.8 | 77.7 | 78.9 | 79.9
 | 60 | NA | 69.0 | 71.1 | 72.4 | 73.5 | 75.6 | 76.7 | 77.5 | 78.9 | 79.9
 | lowest | 66.5 | 69.7 | 71.5 | 72.8 | 73.8 | 75.9 | 76.9 | 77.7 | 78.9 | 79.9