## Slide 1: WF on DL Channel Raster for NR
Qualcomm Incorporated, Ericsson
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1710177
Document for: Approval

## Slide 2: Band n41 raster
Adopt SCS based raster for Band n41

## Slide 3: 100kHz Based Raster
Raster to subcarrier position mapping
  Raster points to the center of the channel
    SC#0 of RB# NRB/2 for even number of RBs
    SC#6 of RB# int(NRB/2)for odd number of RBs

## Slide 4: SCS Based Raster
Raster will be based on absolute frequency values
  The raster positions will be integer multiples of 15kHz for sub6 bands
  The raster positions will be integer multiples of 60kHz for mmWave range bands
Options for raster to subcarrier position mapping
  Raster points to the center of the channel
    SC#0 of RB# NRB/2 for even number of RBs
    SC#6 of RB# int(NRB/2)for odd number of RBs
  Raster points to the SC#0 of RB#0