## Slide 1: Way forward on R15 NB-IoT RRM
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #84bis R4-1711346
Dubrovnik, Croatia, 9 – 13 October, 2017
Agenda Item: 8.20.4

## Slide 2: Agreements on measurement accuracy improvement
RAN4 confirms that NSSS based RRM measurement is feasible under RAN1 working assumption that the ratio of NSSS EPRE and NRS EPRE is configured from {-3, 0, 3, spare}.
  To estimate downlink path loss based on NSSS for uplink power control, UE needs to be informed with the Tx power of NSSS.
Considering the signaling overhead and limited gain in measurement accuracy, it is not encouraged to use the combination of NSSS and NRS for RRM measurement for mobility purpose.

## Slide 3: Agreements on TDD RRM requirements
Categories | Requirements | TDD specific requirements
Section 4 E-UTRAN RRC_IDLE state mobility | Cell selection and reselection | not needed
 | Paging interruption | not needed
 | UE measurement capability | needed
Section 6 RRC Connection Mobility Control | RRC re-establishment | not needed
 | Random access | not needed
 | RRC Connection Redirection to Non-anchor Carrier in NB-IoT | FFS
Section 7 Timing and signalling characteristics | UE transmit timing | not needed
 | UE timer accuracy | not needed
 | Timing advance | not needed
 | Radio link monitoring | not needed
Section 8 UE Measurements Procedures in RRC_CONNECTED State | Intra-frequency measurement | FFS
Section 9 Measurements performance requirements for UE | Measurement accuracy | FFS
 | PHR | not needed
Section A.3 RRM test configurations | NPDCCH RMC pattern | needed
 | NPDSCH RMC pattern | needed
 | NOCNG pattern | needed
Section A.4, A.6 and A.7 | RRM test cases | needed
Section B.1 Conditions for E-UTRAN RRC_IDLE state mobility | Requirements side condition in RRC IDLE mode | needed
Section B.2 Conditions for UE Measurements Procedures in RRC_CONNECTED State | Requirements side condition in RRC CONNECTED mode | needed
Section B.3 Conditions for measurements performance requirements for UE | Side conditions for measurement performance | needed
The need of specific requirements for TDD is as follow