## Slide 1: WF on MPR for Sub-6 NR
Qualcomm Incorporated, Nokia, [Skyworks Solutions], …
3GPP TSG-RAN WG4 #84bis R4-1711559
October 9th ‒ 13th, 2017
Dubrovnik, HR

## Slide 2: Background
Simulations for MPR have been provided in the documents in the references based on assumptions from WF in [8]
  Outer and inner regions for MPR have been defined (definition in [8])
  MPR is the maximum value within each region, for all channel bandwidth and SCS options
  For Pi/2-BPSK, QPSK, and 16QAM, MPR is defined separately for inner and outer regions
  For 64QAM and 256QAM, MPR is common between inner and outer regions

## Slide 3: Way Forward
Tentative values for MPR are provided on the next two slides
Companies are encouraged to verify the tentative MPR values
Additional simulation results to be considered at RAN4 #85 are not precluded
Two (plus one) options for PA calibration
  Two calibration points according to LTE fully allocated QPSK with either 0 or 1 dB MPR.
  A third calibration point (LTE MPR = 0.5 dB for 100 RB QPSK) can also be considered as a compromise.
  At this point, companies can choose their own preference for simulations.
Sufficient data should be provided so that both inner and outer regions can be verified across bandwidths and SCS for different modulations

## Slide 4: MPR (Outer region)
 |  | Nokia (10956) | QC (11468) | HW (10489/90/91/92) |  | 
Allocation type |  | Outer (max MPR) |  |  |  | 
WF type | modulation | MPR For all BW and SCS |  |  | average | agreement
DFT-s-OFDM | PI/2 BPSK | 0 | N/A | 0 | 0 | [0]
 | QPSK | 0.5 | 1.5 | 0.5 | 0.8333333 | [1]
 | 16QAM | 1 | 2 | 1.5 | 1.5 | [1.5]
 | 64QAM | 1 | 3 | 1.5 | 1.8333333 | [2]
 | 256QAM | TBD | 5 | N/A | 5 | [5]
CP-OFDM | QPSK | 2.5 | 3.5 | 3 | 3 | [3]
 | 16QAM | 2.5 | 3.5 | 3 | 3 | [3]
 | 64QAM | 2.5 | 3.5 | 3 | 3 | [3]
 | 256QAM | TBD | 7 | N/A | 7 | [7]

## Slide 5: MPR (Inner region)
 |  | Nokia (10956) | QC (11468) | HW (10489/90/91/92) |  | 
Allocation type |  | Inner (min MPR) |  |  |  | 
WF type | modulation |  |  |  | average | agreement
DFT-s-OFDM | PI/2 BPSK | 0 | N/A | 0 | 0 | 0
 | QPSK | 0 | 0.5 | 0 | 0.1666667 | [0]
 | 16QAM | 0 | 0.5 | 0 | 0.1666667 | [0.5]
 | 64QAM | 1 | 3 | 1.5 | 1.8333333 | [2]
 | 256QAM | TBD | 5 | N/A | 5 | [5]
CP-OFDM | QPSK | 0 | 1.5 | 1 | 0.8333333 | [0.5]
 | 16QAM | 1 | 2 | 1.5 | 1.5 | [1.5]
 | 64QAM | 2.5 | 3.5 | 3 | 3 | [3]
 | 256QAM | TBD | 7 | N/A | 7 | [7]

## Slide 6: References
[1] R4-1710956, “NR range 1 MPR proposal,” Nokia, Nokia Shanghai Bell, Skyworks Solutions, Inc.
[2] R4-1711468, “Simulation results of MPR for Sub6 NR,” Qualcomm Incorporated
[3] R4-1710489, “MPR evaluation for 15kHz SCS for below 6GHz (DFT-S-OFDM),” Huawei, Hisilicon
[4] R4-1710490, “MPR evaluation for 15kHz SCS for below 6GHz (CPOFDM),” Huawei, Hisilicon
[5] R4-1710491, “MPR evaluation for 30kHz SCS for below 6GHz (DFT-S-OFDM), “Huawei, Hisilicon
[6] R4-1710492, “MPR evaluation for 30kHz SCS for below 6GHz (CPOFDM),” Huawei, Hisilicon
[7] R4-1710147, “MPR evaluation for sub 6GHz,” CMCC
[8] R4-1709944, “WF on MPR table and allocation definition for sub-6GHz,” Skyworks Solutions, Inc.