## Slide 1: WF on V2X Resource Reselection Test
Qualcomm Inc.
R4-1711698
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, 21 – 25 Aug, 2017

## Slide 2: WF
  Concentrate on RSSI measurement test first.
  RSRP test can reuse methodology

## Slide 3: Test Setting
T2 = 20 by setting packet delay budget.
Each subframe has 5 sub-channels
  3 High RSSI sub-channels
  1 mid RSSI sub-channel
  1 low RSSI sub-channel
The test verify RSSI requirement by observing the rate of transmission at mid RSSI sub-channel
  If no mistake is made, only low RSSI sub-channel transmission occurs.
  If some mistake is made, mid RSSI sub-channel transmission occurs with some probability
  The requirement is that the rate mid RSSI sub-channel transmission occurs is less than X%

## Slide 4: Test Setting (cont.)
High
High
High
Low
Mid
RSSI
RSSI + 15dBc
RSSI + 15dBc
RSSI + 15dBc
RSSI + 5 + YdBc
Channel BW
Different RSSI levels are set by OCNG
Y is defined by AGC-ADC simulation
X = 20 %

## Slide 5: Simulation Assumption
ADC bit resolution: 9 bits
ADC backoff: 20dBc.
All signal in each sub-channel are OCNG.
For each X: evaluate the error probability that measured RSSI at low sub-channel > measured RSSI at mid-subchannel.
Target X for error probability is 10%.