## Slide 1: WF on transmit diversity on PC5 for advanced receivers
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #84bis Dubrovnik, Croatia, 9 - 13 October 2017
Agenda Item: 8.19
R4-1711724

## Slide 2: Background
RAN1 would like to get feedback on the following aspects due to two-port non-transparent transmit diversity:
  Q1: Impact on PSSCH-RSRP measurement accuracy of Rel-14 UEs
  Q2: MPR for Rel-15 UEs
  Q3: Impact on MMSE MRC receivers and advanced receivers in the a) presence of one interferer (single-port transmission and two-port diversity) b) presence of multiple interferers (single-port transmission and two-port diversity)

## Slide 3: Way forward on Q3
Interference scenarios
  Single-port transmission
  Non-transparent Two-port diversity
Number of interferers
  Single dominant interferer
    INR1 = 0, 5, 10, [15] dB
  Two dominant interferers
    INR1 = 0, 5, 10 dB
    INR1 = INR2 + 3dB
  Other options are not precluded
  Companies are encouraged to bring analysis on number of interferers and its corresponding interference level distribution for V2X scenarios

## Slide 4: Way forward on Q3
Advanced receiver structure
  LMMSE-IRC
  RAN4 group prioritizes the study on the impact of Rel-14 UE
  Other options are not precluded
Propagation condition
  EVA1500
  EVA180
  Other options are not precluded
Other parameters
  Reuse V2X PSSCH test parameters in Section 14.2