## Slide 1: WF on FRC for BS receiver requirements and simulation assumptions
Ericsson, NTT DoCoMo, Huawei, ZTE, CATT, Nokia
3GPP TSG-RAN WG4 RAN4#84b
Dubrovnik, Croatia, 9th-13th October, 2017
R4-1711809
Document for: Approval

## Slide 2: Background
During RAN4#84bis, following parameters contributions provide FRCs proposals based on agreed WF in [1]:
R4-1710993, FRC for RX RF requirements, NTT DoCoMo
R4-1710772, Discussion on REFSENS requirement for FR1 NR BS, ZTE
R4-1710774, Discussion on REFSENS requirement for FR2 NR BS, ZTE
R4-1710197, FRC for BS receiver requirements, Huawei, HiSilicon
R4-1710461, Considerations on FRCs for NR BS REFSENS, CATT
R4-1710876, FRCs for NR Rx requirements, Ericsson
R4-1710770, Discussion on ICS requirement for FR1 NR BS, ZTE
R4-1710771, Discussion on ICS requirement for FR2 NR BS, ZTE
R4-1710769, Discussion on dynamic range requirement for FR1 NR BS, ZTE
R4-1710460, Considerations on FRC of NR FR1 dynamic range, CATT
Based on these contributions and offline discussion, we summarized the following proposals and finalize following agreements.

## Slide 3: Agreement 1: PRBs coverage FR1
For FR1:
  To test all PRBs for every CBW, overlapping of FRCs might be needed.
  When needed, 2 FRC patterns would have to be defined (e.g. as shown here after)
    One first pattern with a certain number of FRCs, leaving gaps of PRB(s).
    A second pattern with, at least, FRCs covering those gaps.
  When RF Conformance (until June 2018) will be addressed, depending on the considered requirement, it shall be agreed if all PRBs shall be tested or not:
    If all PRBs shall be tested: those 2 patterns should be used.
    If not, only the 1st pattern shall be used
  Any other method/proposal is not precluded.
Example

## Slide 4: Agreement 2: PRBs coverage FR2
For FR2:
  Simple combination of 1 FRC shall cover the full channel BW.
  No FRC overlapping would be needed to cover all PRBs according to current agreement.
SCS [kHz] | 50MHz | 100MHz | 200MHz | 400 MHz
 | NRB | NRB | NRB | NRB
60 | 66 | 132 | 264 | N.A
120 | 32 | 66 | 132 | 264

## Slide 5: Agreement 3: Requirements and SCS
BS Rx Requirement shall be specified for each CBW and each SCS:
  - FRC(s) are needed for all SCS.

## Slide 6: Agreement 4: FRCs for FR1
FRCs for FR1
5MHz-15kHz (25)
5MHz-30kHz (11)
10 MHz – 60kHz (11)
20MHz-15kHz (106)
20MHz-30kHz (51)
20MHz-60kHz (24)

## Slide 7: Agreement 5: FRCs for FR2
FRCs for FR2
50MHz-60kHz(66)
50MHz-120kHz(32)
100MHz-120kHz(66)

## Slide 8: Simulation assumptions SNR value - REFSENS and ICS (FR1 and FR2)
Parameter | Value
Propagation | AWGN
Modulation | QPSK
Coding rate | 1/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Criteria | SNR at 95% throughput
TBS (*) | TBD
CRC for TB (*) | 24bits for TB size > 3824 16bits for TB size ≤ 3824
CRC for CB (*) | If more than 1 CB: 24bits
(*): Values would be further discussed via email and agreed by Oct., 27th | 

## Slide 9: Simulation assumptions SNR value – Dynamic Range
Parameter | Value
Propagation | AWGN
Modulation | 16QAM
Coding rate | 2/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Criteria | SNR at 95% throughput
TBS (*) | TBD
CRC for TB (*) | 24bits for TB size > 3824 16bits for TB size ≤ 3824
CRC for CB (*) | If more than 1 CB: 24bits
(*): Values would be further discussed via email and agreed by Oct., 27th | 

## Slide 10: References
[1] R4- 1710044, WF FRCs for Rx requirements, Ericsson, Huawei