## Slide 1: WF on reciever antenna gain
Ericsson
R4-1711812
3GPP TSG- RAN Working Group 4 (Radio) meeting #84bis
Dubrovnik, Croatia, 9-13 October 2017
Agenda Item: 9.5.3.7.1

## Slide 2: Way forward
Background
  Receiver antenna gain is fundamentally related to on the antenna aperture (i.e. GANT=4*pi*Aphys*ea / wavelength2, where ea is the radiation efficiency and Aphy is the antenna aperture)
Way forward
  Clarify what is the minimum expected aperture for each deployment
  Clarify consideration of real aperture aspects such as non contiguous elements
  Clarify what factors are need to derive antenna gain, companies encourage to provide views.
    Some examples of factors to consider are provided in the informative annex for guidance
  Consider further whether more than one requirement per BS class is needed or not
  Companies encourage to provide views if BS with 16dBi will work satisfactory in FR2 with wider BW (large path-loss and low PSD due to wide BW).
Agreements
  Gain is no lower than 16dBi for WA/MR BS (, and 10dBi for Indoor)
    Above estimated values are made considering potential for smaller array (3~6dB lower than 8*16 elements) and/or not all loss factors evaluated (1-3dB)
  This antenna gain value is used to define minimum OTA sensitivity. But for other receiver requirements dependent on each requirement, a different procedure for wanted signal level than re-use of this gain and sensitivitiy may be used.

## Slide 3: Informative annex
This annex is not for approval. It collects a list of factors to consider provided for information. The factors are intended to stimulate discussion and not as a baseline:
  Impact of any needed calibration (phase and amplitude) between receive antennas or RX-TX
  More realistic assumptions on the array design
    The assumptions on the array geometry ( element separation e.g. 0.5 lamda and relations to HPBW) used for the co-existence simulations are very idealistic
    The assumptions on array geometry with respect on sub-element allocation.
    Mutual coupling
    Interaction of factors such as grating lobes, scan loss, radome losses
  Matching and distribution losses within the antenna array
  Element radiation efficiency
  Losses arising from mechanical constraints in antenna fabrication and mechanical tolerances
  Radome losses, which may be directional
  Impact of variation in sensitivity for a fixed beamforming / grid of beams type of implementation
  Baseband algorithm implementation margins
  Any additional filtering needed once OOB blocking etc. is known