## Slide 1: Way Forward on Minimum CHBW and SCS for SS/PBCH
Samsung, NTT DoCoMo, KDDI, Softbank, Verizon, Dish Network, T-Mobile USA, Verizon, AT&T, Qualcomm, Nokia
3GPP TSG-RAN WG4 RAN4#84bis
Dubrovnik, Croatia, 9- 13 Oct, 2017
Agenda: 9.3.1.1
R4-1711817

## Slide 2: Operators’ demand in RAN4 RAN4#84bis (Information collected)
Sub 6 NR Bands | Minimum Channel bandwidth | SS block sub-carrier spacing (Default)
1 | 5 MHz | 15 kHz
3 | 5 MHz | 15 kHz
5 | 5MHz,10MHz | [15kHz,30kHz]
7 | 5 MHz | 15 kHz
8 | 5 MHz | 15 kHz
20 | 5 MHz | 15 kHz
28 | 5 MHz | 15 kHz
41 | 10MHz | [15kHz, 30 kHz]
66 | 5 MHz , 10MHz | [15 kHz, 30kHz]
70 | 5 MHz | 15 kHz
71 | 5 MHz | 15 kHz
1.427-1.518 GHz | 5 MHz | 15 kHz
3.3 – 3.8 GHz | 10 MHz | [30kHz]
3.3 - 4.2 GHz | 10 MHz | [30kHz]
4.4 - 4.99 GHz | [40 MHz] | 30 kHz]
mmWave Bands | Minimum Channel bandwidth | SS block sub-carrier spacing (Default)
24.25 - 27.5 GHz | 50 MHz,100 MHz | 120 kHz ,240kHz
26.5 – 29.5GHz | 50 MHz,100 MHz | 120 kHz ,240kHz
37 – 40 GHz | 50 MHz,100 MHz | 120 kHz,240kHz

## Slide 3: WF (1)
Default SCS(s) for SS block: SCS value(s) UE can be assumed for initial access, decided by per band specific basis and captured into specs
  For Sub 6 GHz, candidate values can be 15kHz or/and 30kHz
  For Above 24 GHz ,candidate values can be 120kHz or/and 240kHz
  When decided default SCS(s), impact on number of SS entries need to be considered carefully

## Slide 4: WF (2)
Default SCS(s) for sub 6GHz
  For LTE refarming band except band 5, band 66 and band 41, fixed default SCS as 15kHz
    For band 5 and band 66, 15kHz and 30kHz as default SCSs
    For band 41, FFS
      Option 1: Fixed as one value either 30kHz or 15kHz
      Option 2: 15kHz and 30kHz as default SCSs
  New frequency ranges :
    N77,N78: 30kHz as default SCS
    N79: 30kHz as default SCS
Default SCS(s) for above 24GHz
  For N257, N258, N260: FFS
      Option 1: Fixed as one value either 120kHz or 240kHz
      Option 2: 120kHz and 240KHz as default SCSs

## Slide 5: RAN1 LS （R1-1719165）

## Slide 6: Background –Previous RAN1 agreements (1/2)
RAN1 agreements in RAN1#87
  For initial access, UE can assume a signal corresponding to a specific subcarrier spacing of NR-PSS/SSS in a given frequency band given by specification.
RAN1 agreements for PBCH and SCS for SS in RAN1#88bis (LS R1-1706717):
  Subcarrier spacing's for PSS/SSS for difference freq. ranges: 15kHz/30kHz for below 6 GHz, and 120kHz/240kHz for above 6 GHz
    Note: RAN1 assumes that RAN4 will decide it depending on frequency ranges
  PSS/SSS sequence length: 127 sub carriers (12PRB)
  PBCH BW: 288 subcarriers (24PRB)
RAN1 agreements for mini CHBW and SS SCS in RAN1#89 (LS R1-1709842):
  RAN1 would like to inform RAN4 that because of the inability of the 50MHz minimum carrier bandwidth to support SS Blocks with 240kHz SCS, RAN1 agreed that a minimum carrier bandwidth value of 100MHz should be supported in addition to 50MHz in order to accommodate SS Blocks with 240kHz SCS for bands, where appropriate in the frequency range from 24 GHz to 52.6 GHz.
  RAN1 would also like to inform RAN4 that because of the inability of the 5MHz minimum carrier bandwidth to support SS Blocks with 30kHz SCS, RAN1 agreed that a minimum carrier bandwidth value of 10MHz should be supported in addition to 5MHz in order to accommodate SS Blocks with 30kHz SCS for bands, where appropriate in the frequency range below 6 GHz.
RAN1 agreements for non-contiguous CA in RAN1 NR AH#2 (LS R1-1711825):
  Usage scenario #4 in R1-1711795 is supported in the context of non-contiguous intra-band carrier aggregation
    Carrier without SS block can be configured for some UEs

## Slide 7: Background –Previous RAN1 agreements (2/2)
  RAN1 agreements for NW adaptation and indication of SCS used for SS block for NSA carrier access in RAN1#90 (LS R4-1710118)
  NR supports NW adaptation and indication of SCS used for SS/PBCH block for NSA carrier access
    RAN1 assumes that NSA carrier is the carrier that UE cannot access without NW assistance information
    UE can assume a single subcarrier spacing of SS/PBCH block per frequency carrier
    In case that target NSA carrier is in below 6 GHz range,
      NW can adapt either 15 kHz or 30 kHz SCS for SS/PBCH block transmission, and NW can indicate selected SCS for SS/PBCH block transmission to UE
    In case that target NSA carrier is in between 6 GHz and 52.6 GHz range,
      NW can adapt either 120 kHz or 240 kHz SCS for SS/PBCH block transmission, and NW can indicate selected SCS for SS/PBCH block transmission to UE
  If there is no indication on SCS used for SS/PBCH block transmission on target NSA carrier, UE assumes default SCS for SS/PBCH block transmission

## Slide 8: Background -Discussions in RAN4#84
Sub 6 NR Bands | Minimum Channel bandwidth | SS block sub-carrier spacing
1 | 5 MHz | 15 kHz
3 | 5 MHz | 15 kHz
5 | 10MHz / 5MHz | [30 kHz/15kHz]
7 | 5 MHz | 15 kHz
8 | 5 MHz | 15 kHz
20 | 5 MHz | 15 kHz
28 | 5 MHz | 15 kHz
41 | 10MHz | 30 kHz
66 | 5 MHz / 10MHz | [15 kHz/30kHz]
70 | 5 MHz | 15 kHz
71 | 5 MHz | 15 kHz
1.427-1.518 GHz | 5 MHz | 15 kHz
3.3 – 3.8 GHz | 10 MHz | [15 kHz/30kHz]
3.3 - 4.2 GHz | 10 MHz | [15 kHz/30kHz]
4.4 - 4.99 GHz | [40 MHz] | 30 kHz
mmWave Bands | Minimum Channel bandwidth | SS block sub-carrier spacing
24.25 - 27.5 GHz | 50 MHz/100 MHz | 120 kHz /240kHz
26.5 – 29.5GHz | 50 MHz/100 MHz | 120 kHz /240kHz
31.8 – 33.4 GHz | 50 MHz/100 MHz | 120 kHz /240kHz
37 – 40 GHz | 50 MHz/100 MHz | 120 kHz/240kHz
Operators’ request in RAN4 #84 captured in below tables：
  For bands which with Minimum Channel bandwidth 5MHz/10MHz, the minimum CHBW is 5MHz across the band, meanwhile 30kHz can only support with equal or above 10MHz CHBW
  For bands which with Minimum Channel bandwidth 50MHz/100MHz, the minimum CHBW is 50MHz across the band, meanwhile 2400kHz can only support with equal or above 100MHz CHBW
In RAN4 #84, some operators raised different demand values for SCS in the same band which target for initial access including band66 and mmWave bands; a LS (R4-1709871) sent to RAN1 asking for potential solutions:
  RAN1 is asked to find a solution how to support the following cases:
  Minimum required channel BW and SS SCS for a Sub-6GHz band are 5MHz and 15 kHz, respectively. An operator plans to operate with 10MHz bandwidth 30 kHz SCS in order to deploy NR/LTE DL co-existence within the same band.
  For bands above 6GHz, the minimum required channel BW and SS SCS are 50MHz and 120 kHz, respectively. An operator, who has at least 100MHz contiguous spectrum, plans to operate with 240 kHz SS SCS within the same band.
  RAN1 is asked to find a solution that shall support the ability for a UE