## Slide 1: Way forward on eFD-MIMO performance requirements
Samsung, Qualcomm, Intel, Ericsson, Huawei
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, 9 - 13 October 2017
R4-1711864

## Slide 2
Introduce test requirements for Class A PMI test cases as below
  24Tx Single PMI test case without density reduction: 3.5 for FDD and TBD for TDD
  24Tx Single PMI test case with density reduction: 3.5 for FDD and TBD for TDD
  32Tx Multiple PMI test case: 4.5 for FDD and TBD for TDD
a=0.00012 can insure positive semi-definite matrix for 3x4x2, a =0.00022 for 4x4x2.
Class A PMI test cases

## Slide 3
  Test metric:
    Throughput ratio between the followed Advanced PMI/RPI and followed Advanced PMI with fixed RPI=0.
    Test point :70%
  MIMO correlation matrix:
    Medium spatial correlation
  MCS and Rank:
    16QAM 1/2 Rank2
  HARQ:
    Option1: 4
    Option 2: 1
  Companies are encouraged to bring results through RAN4 email reflector for above two options to fix test set-up before next RAN4 meeting, and finalize corresponding requirements in RAN4#85 meeting.
PMI/RPI reporting test for the advanced CSI codebook
 | α1 | α2 | β | γ
Medium spatial correlation | 0.3 | 0.3 | 0.6 | 0.2

## Slide 4
Test requirements for Class B density reduction PMI test case.
  FDD mode: 1.1
  TDD mode: FFS
Test requirements for aperiodic CSI-RS test case and multi-shot CSI-RS test cases
  FDD mode: 1.2
  TDD mode: FFS
Test configurations for aperiodic CSI-RS test case and multi-shot CSI-RS test cases (TDD mode)
  Reusing test configurations as 9.4.1.3.2 (8*2 with XP HIGH) (Previous agreements : 4*2 ULA)
Test applicable rules for aperiodic CSI-RS test case and multi-shot CSI-RS test cases
  A UE supporting either multi-shot CSIRS or aperiodic CSIRS is not required to run the legacy single PMI test cases with the periodic CSIRS resource, i.e., 9.4.1.3.1 and 9.4.1.3.2 of TS 36.101
Companies are encouraged to share results in email reflector before next RAN4 meeting to finalize test requirements.
Class B PMI test cases