## Slide 1: WF on absolute ACLR for FR2
Huawei, Hisilicon, NTT DOCOMO, INC., Ericsson
R4-1711927
3GPP TSG-RAN4 Meeting #84bis
Dubrovnik, Croatia, 9 - 13 Oct 2017
Agenda Item: 9.5.3.3.2

## Slide 2: Background
Contributions have been discussed in RAN4#84Bis :
  [1] R4-1710267, Absolute ACLR for FR2, Huawei, HiSilicon
  [2] R4-1711153, Proposals on mmWave NR BS ACLR, Nokia, Nokia Shanghai Bell
  [3] R4-1711486, Proposals on remaining issues on ACLR for mm-wave NR base station, Ericsson

## Slide 3: Way forward on absolute ACLR
One of the following options will be decided in next RAN4 meeting.
Option 1 :
  To adopt -13 dBm/MHz as the absolute ACLR value for Macro BS and [-20 dBm/MHz] for other BS classes.
Option 2 :
  To adopt -13 dBm/MHz for BS with maximum output power PTx ≥ 35 dBm in the frequency range 24.24 – 33.4 GHz and PTx ≥ 33 dBm in the frequency range 37 – 52.6 GHz;
  To adopt [-20 dBm/MHz] for BS with maximum output power PTx < 35 dBm in the frequency range 24.24 – 33.4 GHz and PTx < 33 dBm in the frequency range 37 – 52.6 GHz