## Slide 1: Way forward for CRS-IM related advanced receiver impact analysis for network-based CRS-IM
Ericsson
3GPP TSG-RAN WG4 Meeting #84bis Dubrovnik, Croatia, 9 - 13 Oct, 2017
R4-1711935

## Slide 2: RAN4 observations
For UE without CRS-IM, CRS muting improves demodulation performance

## Slide 3: RAN4 observations
CRS-IC receiver
  Up to now, there is no consensus on performance of legacy CRS-IC receiver in the networks with the network-based CRS mitigation in the neighboring cells
    Companies have different observations for the performance impact from CRS muting, the reason may be:
      Different muting pattern, different implementation of CRS-IC receiver
    Companies are encouraged to bring more analysis to check the performance difference

## Slide 4: RAN4 observations
FFS issues
  Impact on NAICs
  Impact to CCIM Type A/B receivers
  Impact on CRS-IC enable/disable mechanism

## Slide 5: Further investigation
Further investigate CRS-IM receiver with more practical setup
  The simulation assumption in the next slides is updated compared with R4-1708732

## Slide 6: Simulation assumption CRS-IM (for information)
Parameters | value
Bandwidth | 10 MHz
Transmission mode | 3, 9
Number of aggressor cells | 2
Interference level () | 10.45 dB for aggressor cell 1 and 4.6 dB for aggressor cell 2
CRS-IC receiver assumption | Assume full CRS is allocated in the aggressor cells
MCS | 8 and 24
MIMO rank | MIMO rank 1, 2
Resource allocation in serving cell | PRBs 0~9 (Partial resource allocation) PRBs 22~27 (center 6 PRBs) PRBs 0~49 (Full resource allocation)
MIMO configuration | 2x2 (2 CRS APs) Interested companies are welcomed to provide simulation results for 4x2 (4 CRS APs)
Interference modelling | When the CRS is muted, CRS is muted except the center 6 PRBs. When the CRS is not muted, CRS is transmitted across the whole bandwidth. 0% load on interference PDSCH.
CRS muting pattern | Pattern 1: 11111 11111 Pattern 2: 0101010101 “1” stands CRS mute, and “0” stands full-bandwidth CRS Other patterns are not excluded
CRS configuration | Non-colliding CRS is configured
Parameters | value
Bandwidth | 10 MHz
Transmission mode | 3, 9
Number of aggressor cells | 2
 | 10.45 dB for aggressor cell 1 and 4.6 dB for aggressor cell 2
CRS-IC receiver assumption | Assume full CRS is allocated in the aggressor cells
MCS | 8 and 24
MIMO rank | MIMO rank 1, 2
Resource allocation in serving cell | PRBs 0~9 (Partial resource allocation) PRBs 22~27 (center 6 PRBs) PRBs 0~49 (Full resource allocation)
MIMO configuration | 2x2 (2 CRS APs) Interested companies are welcomed to provide simulation results for 4x2 (4 CRS APs)
Interference modelling | When the CRS is muted, CRS is muted except the center 6 PRBs. When the CRS is not muted, CRS is transmitted across the whole bandwidth. 0% load on interference PDSCH.
CRS muting pattern | Pattern 1: 11111 11111 Pattern 2: 0101010101 “1” stands CRS mute, and “0” stands full-bandwidth CRS Other patterns are not excluded
CRS configuration | Non-colliding CRS is configured