## Slide 1: WF on measurement capability and measurement gap for NR
Intel
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711936
Document for: Approval

## Slide 2: Agreement on UE capability for FR1/2 measurements
To do in RAN4#85: introduce measurement gap based requirements for per-UE based measurement gap and FR1/2 independent measurement gap (best effort based)

## Slide 3: Agreement on MGL
For UE supports single and per UE gap, three MGL are introduced, 6ms, [4]ms and 3ms
For UE support independent gap for FR1/2, the following MGL are introduced
  FR1 measurement objects: 6ms, [4]ms and 3ms
  FR2 measurement objects:
    With FR1/LTE serving cell only: 6ms, [4]ms and 3ms
    With FR2 serving cell:
      If identical gap is configured for both FR1 and FR2: 6ms, [4]ms, 3ms,
      If independent gap is configured for FR1 and FR2:[1+x] ms, [2.25+x] ms, [5+x]ms
    Note: x is defined based on RF switching time and TBD in RAN4#85
    Non-NR-capable UE does not need to support new gap other than 3ms or 6ms

## Slide 4: Agreement on MGRP
Four MGRP to be introduced: 20ms, 40ms, 80ms and 160ms for NSA and SA NR UE
  If non-NR measurement objects are configured, 160ms MGRP should not be used
  FFS: 40ms MGRP LTE requirements will apply if 20ms MGRP common gap is configured
  Use of 20ms MGRP configured by LTE PCell needs update to gap pattern IDs supported in 36.133
  For UE not supporting NR, both 20ms and 160ms should not be configured
Necessity of 20ms MGRP +6ms MGL to be confirmed by RAN4#85
To do in RAN4#85:
  Identify the combinations of MGRP and MGL, which are necessarily to be introduced in Rel-15
  Update measurement gap configuration table based on updated MGL and MGRP

## Slide 5: Agreement on intra-frequency measurements for FR1/2
It shall be assumed in release 15 that all UE are not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on FR2 serving cells during FR2 intra-frequency measurements, ie no capability is needed
For UE not supporting mixed numerology scenarios in FR1 and FR2, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH for intra-frequency measurement without RF-retuning

## Slide 6: Agreements on measurement gap configuration
RAN4 is still discussing if gap or other mechanism is used for
  Intrafrequency measurements within the active BW part on FR2 due possible RX beamforming
  Intrafrequency measurements within the active BW part with a different numerology between data/control and SS block
  To do in RAN4#85: study mechanisms on how to handle intra-frequency with no RF-retuning in both FR1 and FR2

## Slide 7: Agreements on gap sharing
Gap sharing between intra-frequency with gap and inter-frequency measurement
  Configurable by NW with up to 4 levels including equal sharing