## Slide 1: 3GPP TSG-RAN WG4 Meeting #85 R4-1712661 Reno, NV (USA), 27th Nov – 1st Dec 2017
Source: Keysight Technologies, MVG Industries
Title: Extension of quiet zone characterization method to include phase characterization
Agenda item: 9.8.2
Document for: Approval

## Slide 2: Objective of this Contribution
This document addresses the method to characterize phase in the quiet zone. The outcome from the characterization would give the as phase ripple/curvature
R4-1711278 presents a TP (TR38810) describing the amplitude ripple characterization procedure for FR2.
  The outcome of the amplitude ripple test gives
    surface standard deviation that effectively predicts the variation of the TRP/TRS measurements
    spherical surface integrals of EIRP/EIS.
The objective of this contribution is to introduce a ‘Characterization of the phase ripple/ curvature in the Quiet Zone’ test procedure.
The reference antenna for the setup is FFS based on certain boundary conditions (R4-1711825)
Once agreement is reached, the TP (R4-1711278) will be appended.

## Slide 3: Contribution to MU due to phase and amplitude variation
Due to the use of phased array in the FR2 both amplitude and phase characteristics of the quiet zone is important to be characterized.
High amplitude or phase variation will cause non-coherent summation of the wave fronts from the individual elements.
The variation of MU due to these variations in the DUT performance depends on the size of the phase array, topology of the array, element type used and the offset distance of the array from center of the quiet zone.
Since the type of antenna and its topology cannot be estimated beforehand due to blackbox approach the following proposal is suggested
Proposal 1: Agree on maximum allowed phase variation allowed in the quiet zone
Observation 1: At a separation distance of 2D2/λ, agreed far field definition, phase taper is 22.5˚.

## Slide 4: Number of Reference Positions and procedure
Any number of positions between the 7 reference points can be selected.
  The resolution of the step size will effectively capture any phase ripple
The 7 extreme positions will highlight the phase taper
It is enough to make this measurement when the reference probe is pointing towards the measurement probe
Any number of positions between the 7 reference points can be selected.
  The resolution of the step size will effectively capture any phase ripple
The 7 extreme positions will highlight the phase taper
It is enough to make this measurement when the reference probe is pointing towards the measurement probe
The phase characterization is a relative measurement
  Place the reference antenna at the center of the QZ and point it straight to the measurement antenna.
  Connect both the antennas to a VNA
  Calibrate this position with through measurement (S21) to set this as 0˚
  Measurement in both polarizations need to be performed.
  Move the reference antenna in the directions P2-P7 with a step size of 0.5˚ and capture S21
Proposal 2: Make phase characterization using vector measurement to highlight phase ripple and taper in the quiet zone
Proposal 3: Make phase measurements with a step size of 0.5˚ for the radius of the quiet zone
Proposal 4: Characterization is to be done for both polarizations individually
Proposal 5: Characterization is to be done for agreed frequency points which is FFS

## Slide 5: Proposals
Proposal 1: Agree on maximum allowed phase variation allowed in the quiet zone
Proposal 2: Make phase characterization using vector measurement to highlight phase ripple and taper in the quiet zone
Proposal 3: Make phase measurements with a step size of 0.5˚ for the radius of the quiet zone
Proposal 4: Characterization is to be done for both polarizations individually
Proposal 5: Characterization is to be done for agreed frequency points which is FFS

## Slide 6: References
R4-1711278, “TP (TR38.810) on Quality of the Quiet Zone Characterization for FR2” Rohde & Schwarz, 3GPP TSG RAN WG4 #84bis, Dubrovnik, Croatia, October 2017
R4-1710077, WF on NR MU and test tolerance, CATR, Intel Corporation, Keysight Technologies, Rohde & Schwarz, Anritsu, 3GPP TSG RAN WG4 NR#3, Nagoya, Japan, September 2017
R4-1707221, Meaning of Quiet Zone in MU discussions, Anritsu, 3GPP TSG-RAN4 WG#84, Berlin, Germany, August 2017
R4-1711825, MVG Industries, 3GPP TSG RAN WG4 #84bis, Dubrovnik, Croatia, October 2017