## Slide 1: Conditions on single Tx switched UL
NTT DOCOMO, INC.
3GPP TSG-RAN WG4#85 Meeting
Reno, Nevada, USA, Nov. 27 - Dec 1, 2017
R4-1713184
Agenda item: 9.4.2
Document for: Approval

## Slide 2: Introduction
  RAN4#84bis approved a WF of R4-1711551.
  Formula’s are used to define which channel combinations within difficult inter-band combinations are not affected by IM2 and 3
    In such case, simultaneous UL is mandatory
  RAN4 still needs to clarify the conditions that a channel combination is defined as “difficult” within difficult inter-band combinations
  For example, RAN4 is going to discuss the definition of UL and DL channels in formula from the following options.
    Alt.1. spectrum holdings of a operator in a band
    Alt.2. aggregated UE channel bandwidth configured by the network
    Alt.3. transmission bandwidth
  Other missing aspects not described in agreed WF also needs to be considered in detail
    NW synchronization and UE measurement
    IMD and DL channel locations in “difficult” channel combination
    IMD impact in time domain

## Slide 3: NW synchronization and UE measurement
Proposal 1:
  If all UE shall not support SSTD measurement for asynchronous NW, all of channel combinations should be defined as “Easy” even in difficult band combination
Background:
  As pointed out in our paper R4-1713185, only synchronous NW has been considered in RAN1 for single Tx switched UL
  To enable time-switching agreed in RAN1 for asynchronous NW, eNB and gNB in DC operation need to share SFN/subframe/slot-boundary timing differences, e.g. obtained by SSTD measurement at UE side
D | D | D | D | D | D | D | D | D | D
U | U | U | U | U | U | U | U | U | U
D | U | D | D | D | D | U | D | D | D
time
In those periods, NW needs to avoid simultaneous UL in LTE and NR if single Tx should be applied
LTE FDD:
NR TDD:
(in async.)

## Slide 4: Definition of DL and UL channels
Proposal 2:
  Define DL and UL channels as Alt.3, i.e. transmission bandwidth
Background :
  Agreed Formula:
    Interference bandwidth: IBW = |a| x CBW1 + |b| x CBW2
      |a| + |b| = 2 (or 3)
      CBW1 and CBW2 are UL channels
    Center frequency of IBW: fIBW = a x f1 + b x f2
      f1 and f2 are center frequency of each UL channel
    The range of IMD 2 (or 3): [fIBW – IBW/2, fIBW + IBW/2]
  Alternatives of UL and DL channels
    Alt.1. spectrum holdings of a operator in a band
    Alt.2. aggregated UE channel bandwidth configured by the network
    Alt.3. transmission bandwidthIn agreed formula, the definition of DL and UL Alt.3. transmission bandwidth
  Actual IMD location is derived by only Alt.3, hence there is no reason to use another alternatives

## Slide 5: IMD and DL channel locations
Proposal 3:
  Channel combination is defined as difficult if more than 50% of DL channel suffers from IMD2 (or 3) in frequency domain
  Specific conditions are described in slide #6 and #7
Background:
  It is still under that relationship between IMD2 (or 3) and DL channel
  Single Tx switch should not be allowed if most of DL channel does not suffer from IMD2 (or 3)
DL channel
IMD2
f
DL channel
IMD2
f
DL
channel
IMD2
Easy
Difficult
Easy
Less than 50%
More than 50%
f
f
f

## Slide 6: IMD and DL channel locations (cont.)
IMD formula (same as previous agreement)
  Interference bandwidth: IBW = |a| x TxBW1 + |b| x TxBW2
    |a| + |b| = 2 （for 2nd order IMD）
  Center frequency of IBW: fIBW = a x f1 + b x f2
    f1 and f2 are center frequency of each UL signal
Terminology
  Rx frequency range: [frx_low, frx_high]
  Rx channel bandwidth: RxBW = frx_high - frx_low
  IMD range: [fIM2_low, fIM2_high] = [fIBW – IBW/2, fIBW + IBW/2] = [a x f1 + b x f2 – (|a| x TxBW1 + |b| x TxBW2) / 2, a x f1 + b x f2 + (|a| x TxBW1 + |b| x TxBW2) / 2]
f
Rx channel
frx_low
frx_high
fIM2_low
fIM2_high
IBW
RxBW
IMD2
fIBW

## Slide 7: IMD and DL channel locations (cont.)
Case | Condition | Example figure
Case1 Easy | - frx_low >= fIM2_high | 
Case2 Easy | - frx_high <= fIM2_low | 
Case3 Easy | - frx_high >= fIM2_high > fIM2_low >= frx_low - IBW < RxBW x 50% | 
Case4 Easy | - fIM2_high >= frx_high >= fIM2_low >= frx_low - fIM2_high – fIM2_low <= RxBW x 50% | 
Case5 Easy | - frx_high >= fIM2_high >= frx_low >= fIM2_low - fIM2_high – frx_low <= RxBW x 50% | 
Case6 Difficult | - other | 
Rx channel
IMD2
Rx channel
IMD2
f
Rx channel
IMD2
Rx channel
IMD2
Rx channel
IMD2
Rx channel
IMD2

## Slide 8: IMD impact in time domain
Proposal 4:
  Define difficult channel considering IMD impact on DL channel in time domain
Background:
  In some cases as shown in blow figures, IMD2 (or 3) does not impact on DL channel in certain time instance
1. Different numerology between LTE and NR
2. Different slot structure
UL
DL
UL
DL
FDD LTE
(15kHz SCS)
DL
DL
TDD NR
(60kHz SCS)
IMD2
Freq.
Time
Subframe (1msec)
slot (0.25msec)
FDD LTE
(15kHz SCS)
TDD NR
(15kHz SCS)
Freq.
Time
D | D | D | D | D | D | D | D | D | D | D | D | D | D
U | U | U | U | U | U | U | U | U | U | U | U | U | U
Subframe (1msec = 14OFDM symbol)
D | D | D | D | D | D | D | D | D | D | D | D | GAP | U
IMD2

## Slide 9: Conclusion
Proposal 1:
  If all UE shall not support SSTD measurement for asynchronous NW, all of channel combinations should be defined as “Easy” even in difficult band combination
Proposal 2:
  Define DL and UL channels as Alt.3, i.e. transmission bandwidth
Proposal 3:
  Channel combination is defined as difficult if more than 50% of DL channel suffers from IMD2 (or 3) in frequency domain
  Specific conditions are described in slide #6 and #7
Proposal 4:
  Define difficult channel considering IMD impact on DL channel in time domain