## Slide 1: Way forward for CRS-IM related advanced receiver impact analysis for network-based CRS-IM
Ericsson
3GPP TSG-RAN WG4 Meeting #85 Reno, USA, Nov. 27 – Dec. 1 2017
R4-1713897

## Slide 2: RAN4 observations
For legacy UEs with CRS-IM, RAN4 has the following observations:
  Legacy UEs with CRS-IM receivers are unaware on neighbouring cell CRS muting and perform CRS-IM receive processing under assumption that neighbouring cell CRS signals are present
  CRS-IC with muted BW CRS in aggressor cell has performance impact compared with CRS-IC with full BW CRS in aggressor cell
    The impact is implementation dependent and scenario dependent.
      Some companies observed 1~2 dB degradation at least for some scenarios
      Some companies observed negligible performance degradation
It is beneficial for UE to get network assistance on the CRS muting in the neighbouring cells

## Slide 3: RAN4 observations
Impact to CCIM Type A/B receivers
  Neighboring cell CRS muting has limited impact on the CCIM receivers performance under practical conditions.
Impact on NAICs
  For legacy NAIC UE, some degradation may be expected

## Slide 4: RAN4 conclusions
As a conclusion of the analysis of Objective #1 and Objctive #2 of the WID (R4-171408), RAN4 sees beneficial for UE to be aware of whether neighbouring cells use CRS muting or not
RAN4 agreed to introduce signalling to inform Rel-15 UEs that neighbouring cells use CRS muting.
  Signalling details are FFS.