## Slide 1: WF on Extended-Band12
Dish
R4-1714000
3GPP RAN4#85
Reno, US, 27th Nov -1st Dec

## Slide 2: Simulations for RAN4#86
Non-collocation between B29 and Extended B12 always assumed
B29 rural, Extended B12 rural or urban macro
  Cell size [10]km for rural, [TBD]km for urban macro
  Tower height [45m] for Rural, [30m] for urban macro
1-4 NB-IOT RB’s within first 1MHz of A block + LTE within B12
  3GPP and FCC emission requirements must naturally be met
Two different BS power distribution assumptions:
Equal PSD across NB-IOT and LTE
43dBm for NB-IOT (equal PSD across NB-IOT when multiple RB’s) and 43dBm for LTE
Evaluate the reduction in B29 cell size based on 5% percentile SINR drop and use that as a criteria to assess the impact in Extended B12 specifications

## Slide 3: Simulations table
B29 | Extended B12 | BS TX power | Notes
RURAL | RURAL | 43dBm, equal PSD over LTE and NB-IOT CC’s | PSD for LTE RB’s and NB-IOT RB’s =43dBm-10log10(51…54)
RURAL | URBAN MACRO | 43dBm, equal PSD over LTE and NB-IOT CC’s | PSD for LTE RB’s and NB-IOT RB’s =43dBm-10log10(51…54)
RURAL | RURAL | 43dBm for LTE and 43dBm for NB-IoT CC’s | PSD for LTE RB’s =43dBm-10log10(50) PSD for NB-IOT RB’s =43-10log10(1…4)
RURAL | URBAN MACRO | 43dBm for LTE and 43dBm for NB-IoT CC’s | PSD for LTE RB’s =43dBm-10log10(50) PSD for NB-IOT RB’s =43-10log10(1…4)