## Slide 1: WF on 1 RX CRS-IM performance
Intel Corporation, Qualcomm
3GPP TSG-RAN WG4 Meeting #85 Reno, Nevada, 27 November – 1 December 2017
Agenda Item: 8.29
R4-1714265

## Slide 2: Cat1bis Performance Requirements
Test cases for 1RX CRS-IM Cat1bis performance requirements
  PDSCH test cases
    Test #1:
      TM4, 4 CRS APs, 24 PRBs, MIMO Rank 1
      FRC: 64QAM (MCS20)
      Interference loading: 20%
      Beamforming model: Follow PMI
    Test #2:
      TM9, 2 CRS APs, 24 PRBs, MIMO Rank 1
      FRC:
        Option 1: 64QAM (MCS20)
        Option 2: QPSK (MCS9)
      Interference loading: 10%
      Beamforming model: Random PMI
  PDCCH test cases
    Test #1: PDCCH, 2 CRS APs, CFI = 1
      Select between AL2 and AL4 after simulation alignment
    Test #2: PDCCH AL4, 4 CRS APs, CFI = 2

## Slide 3: CatM2 Performance Requirements
Test cases for 1RX CRS-IM CatM2 performance requirements
  PDSCH test cases
    CE mode A
    No repetitions and no frequency hopping
    Test #1:
      TM6 with 4 CRS APs, MIMO Rank 1
      FRC: 16QAM (MCS14)
      Interference loading: 20%
    Test #2:
      TM6 with 2 CRS APs, MIMO Rank 1
      FRC: 16QAM (MCS14)
      Interference loading: 10%
  MPDCCH test cases
    CE mode A
    No repetitions and no frequency hopping
    Test #1: MPDCCH AL4, [0%, 10%] interference loading
    Test #2: MPDCCH AL16, 10% interference loading
  FFS if test cases with repetitions and frequency hopping shall be considered

## Slide 4: UE Features/Capabilities
Differentiate UE features to perform CRS-IM for 2/4 CRS APs and for Data/Control channels to allow sufficient UE implementation flexibility
  UE capabilities signalling is FFS