## Slide 1: WF on gap for intra-frequency measurement
NTT DOCOMO
3GPP TSG-RAN WG4 RAN#85
Reno, US, November 27th- December 1st, 2017
R4-1714288
Document for: Approval

## Slide 2: Background
Agreements in RAN4#84bis regarding intra-frequency measurement in FR1 and FR2
It shall be assumed in release 15 that all UE are not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on FR2 serving cells during FR2 intra-frequency measurements, i.e., no capability is needed
For UE not supporting mixed numerology scenarios in FR1 and FR2, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH for intra-frequency measurement without RF-retuning
Agreements in RAN4#85 regarding RX beam switching in FR1
RX beamforming switch in FR1 should not introduce interruption

## Slide 3: Discussion
RAN4 needs to clarify UE behavior in following 3 cases
  Case 1: intra-frequency measurement in FR1 where SCS of SSBs and SCS of serving cell’s data are different and when UE does not support simultaneous reception of SSB and data with mixed numerologies
  Case 2: intra-frequency measurement in FR2 where SCS of SSBs and SCS of serving cell’s data are same
  Case 3: intra-frequency measurement in FR2 where SCS of SSBs and SCS of serving cell’s data are different and when UE does not support simultaneous reception of SSB and data with mixed numerologies

## Slide 4: Analysis for Case 1
Cells within a carrier may or may not be synchronized
  In asynchronous case, cells would apply 5 ms SS burst set periodicity so that 5 ms SMTC window can cover all SSBs from asynchronized cells
UE can be informed about followings for measurement on the carrier
  useServingCellTimingForSync: whether cells within the carrier are synchronized or not
  SSB-measured: which SSB location(s) are to be measured (single bitmap indication applicable to all cells)
Observations
  When cells are not synchronized, whole symbols/slots within SMTC window duration are not available for PDCCH/PDSCH/PUCCH/PUSCH
  When UE is informed that cells are synchronized, only SSB symbols to be measured within SMTC window duration are not available for PDCCH/PDSCH/PUCCH/PUSCH assuming numerology switching does not cause any interruption
5 ms SMTC window
Serving cell
Neighbor cells
e.g., 4 ms SMTC window
Not available for data/cont
Not available for data/cont
Async case
Sync case

## Slide 5: Analysis for Case 2
Cells within a carrier are synchronized (only TDD bands in FR2)
UE can be informed about followings for measurement on the carrier
  useServingCellTimingForSync
  SSB-measured
Different UEs may have different interruption time duration due to RX beam switching
  UEs capable of fast RX beam switching would have interruption time less than CP duration
  UEs not capable of above fast RX beam switching may have interruption time of one or a few symbols duration
There would be some slots that does not contain SSB location within SMTC window (according to SS burst set composition for 120/240 kHz SCS)
5 ms
0.5 ms
120 kHz SCS case
240 kHz SCS case (slot size is based on 120 kHz SCS for data/cont)
5 ms
0.5 ms

## Slide 6: Analysis for Case 2
Observations
  For UE capable of fast RX beam switching, only SSB symbols to be measured within SMTC window duration are not available for PDCCH/PDSCH/PUCCH/PUSCH
  For UE not capable of fast RX beam switching, SSB symbols to be measured and some additional symbols (before/after SSB symbols) are not available for PDCCH/PDSCH/PUCCH/PUSCH
e.g., 3 ms SMTC window
Not available for data/cont
Not available for data/cont
e.g., 3 ms SMTC window
Not available for data/cont
Not available for data/cont

## Slide 7: Analysis for Case 3
In terms of mixed numerology, we can assume same analysis with sync scenario in Case 1 (assuming FR2 only has sync scenario)
In terms of RX beam switching, we can assume same analysis with Case 2
Irrespective of mixed numerology scenario support, same analysis with Case 2 can be applied
Observations:
  Irrespective of mixed numerology scenario support,
    for UE capable of fast RX beam switching , only SSB symbols to be measured within SMTC window duration are not available for PDCCH/PDSCH/PUCCH/PUSCH
    for UE not capable of fast RX beam, SSB symbols to be measured and some additional symbols (before/after SSB symbols) are not available for PDCCH/PDSCH/PUCCH/PUSCH

## Slide 8: Analysis for RSRQ/SINR measurement
Even though main use-case of RSRQ/SINR measurement is inter-frequency, it is possible to configure intra-frequency RSRQ/SINR measurement
In FR2, RSSI/interference are measured with RX beamforming which is used for RSRP measurement
Therefore, RSSI/interference measurement time resource are also not available for PDCCH/PDSCH/PUCCH/PUSCH
  RSSI measurement time resource can be configured by NW
  Default RSSI measurement time resource is still discussed in RAN1
  IMR time resource is confined within SSB symbols

## Slide 9: Proposals
Update agreements made at RAN4#84bis regarding intra-frequency measurement in FR1 and FR2 as follows
  In FR1 intra-frequency SS-RSRP/RSRQ/SINR measurement:
    For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured within SMTC window duration if useServingCellTimingForSync is enabled
    For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within SMTC window duration if useServingCellTimingForSync is not enabled

## Slide 10: Proposals
  In FR2 intra-frequency SS-RSRP/SINR measurement:
    For UE capable of fast RX beam switching, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured within SMTC window duration (if useServingCellTimingForSync is enabled)
    For UE not capable of fast RX beam switching, down-select from following two options
      Option 1: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within slots containing SSB symbols to be measured within SMTC window duration (if useServingCellTimingForSync is enabled)
      Option 2: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, X symbol(s) before each consecutive SSB symbols and X symbol(s) after each consecutive SSB symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
        X = [1] symbol for 60 kHz SCS and [2] symbols for 120 kHz SCS
    Introduce UE capability signaling regarding fast RX beam switching
      Send LS to RAN2

## Slide 11: Proposals
  In FR2 intra-frequency SS-RSRQ measurement:
    For UE capable of fast RX beam switching, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured and RSSI measurement symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
    For UE not capable of fast RX beam switching, down-select from following two options
      Option 1: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within slots containing SSB symbols to be measured and/or RSSI measurement symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
      Option 2: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, RSSI measurement symbols , X symbol(s) before each consecutive SSB/RSSI symbols and X symbol(s) after each consecutive SSB/RSSI symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
        X = [1] symbol for 60 kHz SCS and [2] symbols for 120 kHz SCS