## Slide 1: WF on SSTD measurement for EN-DC when PSCell is not configured
NTT DOCOMO, […]
3GPP TSG-RAN WG4 RAN#85
Reno, US, November 27th- December 1st, 2017
R4-1714399
Document for: Approval

## Slide 2: Background
Agreements in RAN2#85 regarding SSTD measurement are as follows:
  1: The network can configure the NR SSTD measurement whenever a NR PSCell is configured
  2: NR SSTD measurement reporting is extended for cells that are not yet configured in the case that no NR PSCell is configured
  3: Introduce one new capability indicator for SSTD measurement for EN-DC when PSCell is configured.
  4: Introduce one new capability indicator for SSTD measurement for EN-DC when PSCell is not configured.
RAN2 will send LS to RAN4.

## Slide 3: Proposal
SSTD measurement requirements for EN-DC when PSCell is not configured shall be defined in RAN4.
How to perform SSTD measurement should be discussed in next meeting.
  Interesting companies are encourage to bring views on this topic in next meeting.

## Slide 4: Proposed solutions (just for information)
Option 1: Based on SS burst set periodicity of target NR cell(s), network configures special long measurement gap for SSTD measurement for EN-DC when PSCell is not configured.
  For example, 20ms + RF retuning time gap is configured when SS burst set periodicity is 20ms.
Option 2: UE performs SSTD measurement for EN-DC without measurement gap when PSCell is not configured.
Option 3: Reusing LTE measurement gap pattern.
Other solutions are not precluded.