## Slide 1: Way Forward on RRM with Network-Based CRS Interference Mitigation
Ericsson, …
3GPP TSG-RAN WG4 Meeting #85 R4-174419
Reno, Nevada, USA, November 27th – December 1st 2017
Agenda Item: 8.28.2

## Slide 2: General
As a conclusion of the analysis of Objective #1 and Objective #2 of the WID (RP-171408), RAN4 sees beneficial for Rel-15 UE to be aware of whether network-based CRS interference mitigation is used by serving and neighbor cells in the area
  Inform RAN2 about the need for signaling identified in RAN4#85
    Signaling details are FFS and to be provided to RAN2 in RAN4#86
    Solutions based on existing signaling are no precluded, e.g., based on MIB
As per Objective #3 of the WID, specify the conditions (in terms of warm-up and cool-down subframes) under which Rel-15 UE RRM requirements can be met if network-based CRS interference mitigation is used, for both RRC_IDLE and RRC_CONNECED
For Rel-14 and earlier UEs some degradation may be expected, since some UE implementations may rely on a long warm-up time which was not precluded by the standard since Rel-8
RAN4 will further analyze the number of warm-up and cool-down subframes for different scenarios for both Rel-15 UE and Rel-14 (and earlier) UE

## Slide 3: Annex: Background information from WID in RP-171408
Objective #1:
Identify cases, where the network can mitigate CRS, including (but not limited to):
  In IDLE mode the network transmits CRS only on the inner six PRBs with the exception of the following scenarios when the network transmits CRS on full bandwidth:
    Paging occasions
    SIB transmissions
    RACH procedure
  In CONNECTED mode (in addition to the IDLE mode cases) the network transmits CRS only on the inner six PRBs with the exception of the following scenarios when the network transmits CRS on full bandwidth:
    Without DRX configured or when DRX is inactive
    HARQ retransmissions in DL
    PHICH transmissions
    Scheduling request via PRACH or PUCCH
    PRACH due to handover
    MPDCCH monitoring windows
    CRS being used for positioning
  For CA if any PCell, PSCell or activated SCell is in any of the above conditions

## Slide 4: Annex: Background information from WID in RP-171408 (cont.)
Objective #2:
Identify impact, if any, to the following legacy UE procedures when network-based CRS mitigation is used in the network, and potential solutions to mitigate or avoid impact on these legacy UE procedures:
  UE receivers performing CRS based interference mitigation in CONNECTED mode e.g.
    CRS interference mitigation (CRS-IM) receiver, NAICS receiver and Type A and B DL control channel IM receivers.
  UE RRM procedures in IDLE and CONNECTED modes defined in TS 36.133.
  Objective #3:
For cases identified in the objective #1, specify the corresponding RRM core requirements, and, if necessary, specify the identified potential solutions in objective #2.