## Slide 1: WF on spherical coverage in FR2
Samsung, Apple, LGE, Intel, Oppo, Xiaomi, Vivo, MediaTek…
R4-1714355
3GPP TSG-RAN WG4 Meeting #85
Reno, Nevada, USA, November 27 – December 1, 2017
Agenda: 9.4.3.1.3

## Slide 2
A WF on power class was agreed in RAN4#84B [11]
UE vendors have expressed concern about the ideal assumptions
In RAN4#85, the vendors have exchanged simulation results with practical assumptions and have proposed harmonization
RAN4 discussed the difficulty of reaching agreements in RAN4#85
The work plan is revised for the spherical coverage requirement to meet the Rel-15 time frame
Background – Work plan

## Slide 3
Network simulations are required to analyze performance impact and understand tradeoff of spherical coverage
  TR 38.803 does not explicitly address spherical coverage impact/requirement
Network simulation should incorporate realistic assumptions on network architecture and UE constraints
  Modeling must be reasonably aligned between companies
Background – Network performance analysis

## Slide 4
Work plan for spherical coverage has been agreed in RAN4#85 as follows:
  Initiate offline and email discussion (after RAN4#85) on the use cases and model assumptions for NW performance analysis
  RAN4 NR AH #4 (January ’18)
    Initial discussion of simulation results (Both EIRP CDF and Network) based on the harmonized assumptions in this way forward.
    Propose harmonized NW model assumptions and update based on preliminary analysis.
  RAN4 #86 (February ’18)
    Deadline to submit the EIRP CDF simulation results based on the harmonized assumptions. Target preliminary EIRP CDF spherical requirement, based on the simulation outcomes.
    Continue to improve the NW simulation accuracy reflecting initial EIRP CDF requirement (from AH #4)
    Initial discussion of measurement results for prototype devices
  RAN4 #86bis (April ’18)
    Continue to improve the NW simulation accuracy reflecting preliminary EIRP CDF requirement (#86)
    Continue to improve the prototype measurement effort and compare to preliminary EIRP CDF simulation
  RAN4 #87 (May ’18)
    Finalize the spherical coverage requirement for handheld UEs based on the contributions
WF (1) – Work plan

## Slide 5: WF (2) – Assumptions for EIRP CDF
Assumptions for RAN4 NR-AH#4 has been agreed in RAN4#85 based on inputs as noted in Appendix in this WF
  UE vendors are encouraged to submit their contribution that shall include all six assumptions as below
 |  | Assumptions1 | Assumptions2 | Assumptions3 | Assumptions4 | Assumptions5 | Assumptions6 | Notes
Frequency range |  | n257 | n257 | n257 | n257 | n257 | n257 | 
# of antenna in an antenna module/set (# of patches, # of dipoles, etc.) |  | - | - | - | - | - | - | Depends on the current implementation
# of antenna module/set in total |  | 1 | 1 | 2 | 2 | 3 | 3 | 
Finite UV test points |  |  |  |  |  |  |  | Finite test point shall be the baseline
Beam phase shifter controller | degree | 45 | 45 | 45 | 45 | 45 | 45 | Finite beam shall be the baseline
Antenna type (patch, dipole, or both) |  | - | - | - | - | - | - | Depends on the current implementation
Antenna module/set location (front, back, top-side, left-side, right-side, bottom-side) |  | Top / Bottom | Top / Bottom | Top & Bottom | Top & Bottom | Left & Right & Bottom | Left & Right & Bottom | combination of the lists are not precluded.
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Plastic | 
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Plastic | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | Plastic | Metal | Metal | Metal | Plastic | Legacy antenna performance degradation by mutual coupling w/ NR antenna or vice versa.
Device size (WxHxD) | cm3 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | This is for information
Display panel – Full (Y) or Partial (N) | Y/N | Y | Y | Y | N | Y | Y | 
Bezel Margin | mm | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability

## Slide 6
Gap 1, H2 mm
Antenna substrate, H4 mm
Patch antennas, H5 μm
Gap 2, H6 mm
Edge Material 1, W1 mm
Display, H1 mm
Edge material 4, H7 mm
Ground plane, H3 μm
Distances from antennas to any material (d1 and d2) must be carefully noted, specially those in the direction of radiation (H6)
Properties needed for simulation are: dielectric constant ɛr and dielectric loss tan δ
  since both parameters are frequency dependent, companies should consider the frequency at which these are reported in spec sheet, or were characterized
Layer Properties |  |  |  | 
Name | Material | Thickness | Ɛr | tan δ
Display | glass | H1 |  | 
Gap 1 | air | H2 | 1.00 | 0.000
Ground plane | copper | H3 | conductivity | 
Antenna substrate | TBD | H4 |  | 
Antennas | copper | H5 | conductivity | 
Gap 2 | air | H6 | 1.00 | 0.000
Edge material 1 | Plastic/glass/metal | W1 |  | 
Edge material 2 | Plastic/glass/metal | W2 |  | 
Edge material 3 | Plastic/glass/metal | W3 |  | 
Edge material 4 | Plastic/glass/metal | W4 |  | 
Device Cross-Section
Edge Material 2, W2 mm
Edge Material 3, W3 mm
d1 mm
d2 mm
WF (3) - EIRP CDF simulation environment

## Slide 7
Two approaches ([7], [10]) are discussed in RAN4#85.
Assumptions for NW performance analysis to be discussed by email after RAN4#85 for the inputs below:
Operators to provide guidance on deployment scenarios and use cases
  In absence of guidance TR 38.803 scenarios to be considered
  The minimum UE peak EIRP adopted in the simulation shall be modified in accordance with outcome of RAN4#85
The following modeling confirmation or enhancements to 38.803 assumptions are needed to assess impact of spherical coverage on network. The list of parameters which can be modified include (but not limited to)
  ISD
  UE indoor/outdoor ratio (All UEs indoor for Indoor Office, All UEs outdoor for dense urban and Macro)
  Coverage definition and coverage requirement (currently outage is defined as min SINR less than -10dB)
  UE elevation (It is currently fixed at 90 degree)
  Reference antenna pattern CDFs that parameterizes (percentile, EIRP) the spherical coverage requirements (FFS)
  Partial resource allocation (Not allocating all PRBs to UE) (FFS)
  Body Blockage, Handgrip, cover materials (FFS)
All modifications compared to the baseline in TR 38.803 need to be documented
Performance metrics
  Guidance from operators is requested for given deployment scenarios and use cases
  DL and UL throughput, outage
WF (4) – Assumptions for NW Analysis

## Slide 8: Appendix – Information from RAN4#85
 |  | Samsung | Qualcomm |  | Apple | LGE
 |  | R4-1711036 | R4-1712381, R4-1712387 |  | R4-1713850 | R4-1713193
Frequency range |  | n257 | n257 |  | n257 | n257
# of antenna in an array (# of patches, # of dipoles, etc.) |  | Two 2x1 dipole & One 2x2 Patch | N/A | N/A | One 4x1 Patch | One 1x4 dipole / One 1x4 patch
# of arrays in total |  | 2 | 2 | 3 | 2 | 3
Elevation & azimuth angle | degree | 1 degree | N/A | N/A | 1 degree | 1 degree
Beam phase shifter controller | degree | 45 degree (3-bit) | Infinite (-2dB w/ finite beam) | Infinite | 45 degree (3-bit) | N/A
Antenna type (patch, dipole, or both) |  | Both | N/A | N/A | Patch | Both
Antenna location (front, back, top-side, left-side, right-side, bottom-side) |  | Top & Bottom | N/A | N/A | Back & Back | Left & Top & Bottom
Device case material (Plastic, Glass, Ceramic, Metal) | dB | Glass | Glass | Plastic | Glass | Metal
Legacy Antenna (w/ Metal, Plastic Frame) |  | Metal | Plastic | Plastic | Metal | Plastic
Device size (3D) | cm3 | N/A | 66.6 | 66.6 | 53.8 | N/A
Display panel | Y/N | Y | Y | Y | Y | Y
Bezel Margin | Y/N | Y | N/A | N/A | N/A | N/A
Gap between antenna & housing | mm | N/A | N/A | N/A | 1.5 | N/A
Peak EIRP over the sphere | dBm | Max | Max | Max | Max | Max
50 %CDF | dBm | Max-6dB | Max-6dB | Max-5dB | Max-12dB | Max-14dB
20 %CDF | dBm | Max-15dB | Max-11dB | Max-9dB | Max-18dB | Max-20dB

## Slide 9
 | TDoc | Title | Source
[1] | R4-1711036 | Consideration of EIRP spherical coverage requirement | Samsung, Apple, Intel
[2] | R4-1713193 | Further evaluation on NR UE power class at mmWave | LG Electronics
[3] | R4-1712701 | Discussion on mmWave spherical coverage | Dish Network
[4] | R4-1712377 | Further consideration of EIRP spherical coverage | Samsung
[5] | R4-1712381 | Spherical coverage of realistic design | Qualcomm
[6] | R4-1713850 | Consideration of EIRP spherical coverage requirement | Apple
[7] | R4-1712382 | Impact of UE Spherical coverage to network performance | Qualcomm
[8] | R4-1712387 | mmW Spherical Coverage requirements | Qualcomm
[9] | R4-1712811 | CDF spherical coverage requirements for mmWave OTA | NTT DOCOMO
[10] | R4-1713849 | Network performance impact of practical peak EIRP | Apple
[11] | R4-1711895 | WF on power class in FR2 | 
References