## Slide 1: WF on SS Raster
Qualcomm Incorporated
3GPP TSG-RAN WG4 RAN#85
Reno, U.S.A, November 27th-December 1st, 2017
R4-1714514
Document for: Approval

## Slide 2: Subcarrier Mapping
Sync raster will indicate the position of RE=#0(subcarrier #0) of RB#10 of the SS block

## Slide 3: SS Raster Definition for the 0-2.65GHz range
SS Raster is defined as:
  Raster entry=N*900kHz+ M*5kHz, N=1:[2944], M=-1:1
  Raster entry numbering is in increasing order of frequency (first entry=895kHz, entry #2=900, entry #3=905, entry#4=1795kHz…)
  Total number of entries [8832]
Raster applies to bands with 100kHz channel raster and 15kHz channel raster with 5MHz minimum bandwidth(bands might be defined in the future) in this frequency range
For 10MHz minimum channel bandwidth a down selection factor of [6](1 entry in [6]) is used

## Slide 4: SS Raster Definition for the 2.4-24.25 GHz range
SS Raster is defined as:
  Raster entry= 2400MHz+N*1.44MHz,N= 0:[15173]
  Raster entry numbering is in increasing order of frequency
  Total number of entries [15174]
Raster applies to bands with 15kHz channel raster and 10MHz minimum bandwidth(n41, n77,n78, n79, etc) in this frequency range
For 10MHz minimum channel bandwidth and 15kHz SS block SCS a down selection factor of [3] is applied
For 40MHz minimum channel bandwidth and 30kHz SS block SCS a down selection factor of [21]

## Slide 5: SS Raster Definition for the 24.25-100GHz range
SS Raster is defined as:
  Raster entry=[24250.08] MHz+N*[17.28]MHz, N= 0:[4383]
  Raster entry numbering is in increasing order of frequency
  Total number of entries [4384]
Raster applies to bands with 60kHz channel raster in this frequency range
For 100MHz minimum channel bandwidth and 240kHz SS block SCS a down selection factor of [2] can be used