## Slide 1: Wayforward on UE measurement gap for NR
Intel, Samsung, Nokia, Nokia Shanghai Bell, Huawei, HiSilicon, CMCC, […]
3GPP TSG-RAN WG4 RAN#86
Athens, Greece, Feb 26th- Mar 2nd, 2018
R4-1801829
Document for: Approval

## Slide 2: Agreement on Gap sharing between intra-frequency and inter-frequency measurements
All the UE activities for consideration (all the activities are SSB based)
  RLM
  Measurement type A: Intra-frequency measurement w/o MG and w/o interruption
    For FR1, no mixed numerologies is assumed for this measurement type
    For FR2, this measurement type is not applicable
  Measurement type B: intra-frequency measurement with interruption
    For FR1, mixed numerologies is assumed for this measurement type
    For FR2, Rx beam sweeping is assumed for this measurement type
  Measurement type C: intra-frequency measurement with MG
    E.g. Intra-frequency measurement outside active BWP
  Measurement type D: inter-frequency measurement and inter-RAT measurement
  All the scenarios for consideration
    Fully overlapped scenarios:
      Scenario 1a: Fully overlapped between MG and SMTC in type A
      Scenario 1b: Fully overlapped between MG and SMTC in type B
      Scenario 1c: Fully overlapped between MG and RLM
    Partial overlapped scenarios:
      Scenario 2a: Partial overlapped between MG and SMTC in type A
      Scenario 2b: Partial overlapped between MG and SMTC in type B
      Scenario 2c: Partial overlapped between MG and RLM
    Fully non-overlapped scenarios:
      Scenario 3a: Fully non-overlapped between MG and SMTC in type A
      Scenario 3b: Fully non-overlapped between MG and SMTC in type B
      Scenario 3c: Fully non-overlapped between MG and RLM

## Slide 3: Agreement on Gap sharing between intra-frequency and inter-frequency measurements
  No requirement will be defined for scenarios 1c.
  In fully overlapped scenarios 1a/1b,
  FFS: Which scenarios could be avoided by network configuration?
  In partial overlapped scenarios 2a/2b/2c,
  Denoted by NA (Not Applicable)
    For those scenarios can be certainly avoided by NW, the corresponding requirements aren’t needed.
  FFS the expected UE behavior and corresponding requirements for the possible scenarios in the above table.
FR1/FR2 | Within MG only | within/outside MG | Outside MG only
2a(Type A) | NA for FR1 (Note-1) | FFS for FR1 (Note-1) | FFS for FR1 (Note-1)
2b(Type B) | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2
2c(RLM) | NA for FR1/FFS for FR2 | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2
*Note-1: There is no Type-A measurement in FR2, hence the corresponding requirements aren’t needed |  |  | 

## Slide 4: Agreement on Gap sharing between intra-frequency and inter-frequency measurements
  In fully non-overlapped scenarios 3a/3b/3c,
  In scenario 3c: RLM will be conducted on all the available RLM-RS occasions
  In scenario 3a: type A measurement will be conducted on all the available SMTC occasions
  In scenario 3b:
      FFS the impact on UE performance on measurement and data Tx/Rx in case network configure this scenario for type B for small MGRP cases (e.g. 20ms)
  FFS: which of UE activities (RLM/type A/type B/type C/type D) the gap sharing table (between intra-frequency and inter-frequency measurements) will be applied to?
  FFS: the gap sharing table would be finalized in RAN4 #86bis meeting
  Companies are encouraged to provide the insights in RAN4 #86bis meeting.

## Slide 5: Annex
Fully overlapped scenarios
  Scenario 1a: All the occasions of Type A measurement are overlapped with MG
  Scenario 1b: All the occasions of Type B measurement are overlapped with MG
  Scenario 1c: All the occasions of RLM are overlapped with MG
Partial overlapped scenarios
  Scenario 2a: Some of occasions of Type A measurement are overlapped with MG while other occasions of Type A measurement are outside the MG
  Scenario 2b: Some of occasions of Type B measurement are overlapped with MG while other occasions of Type B measurement are outside the MG
  Scenario 2c: Some of occasions of RLM are overlapped with MG while other occasions of RLM are outside the MG
Fully non-overlapped scenarios
  Scenario 3a: None of the occasion of Type A measurement is overlapped with MG
  Scenario 3b: None of the occasion of Type B measurement is overlapped with MG
  Scenario 3c: None of the occasion of RLM is overlapped with MG