## Slide 1: Way forward on eV2X RRM requirements
Huawei, HiSilicon, CATT
3GPP TSG-RAN WG4 Meeting #86 R4-1803097
Athens, Greece, Feb 26th– Mar 2nd, 2018
Agenda Item: 6.17.3

## Slide 2: Agreements on V2X Carrier Aggregation
MRTD and MTTD for V2X non-contiguous CA
  No need to introduce MRTD and MTTD requirements for V2X non-contiguous CA in Rel-15
V2X Synchronization Reference Source selection/reselection requirements for V2X sidelink CA will be introduced in new section
  Requirements in new section focus on the case that a synchronization carrier(s) has been determined by the UE following procedure in RAN1 spec.
    The existing measurement requirements for a detectable intra-frequency V2X SyncRef UE are applied only for the aggregated V2X carrier(s) configured as the synchronization carrier.
    FFS the dropping related requirements for all the component carriers used for V2X CA.

## Slide 3: Agreements on V2X Carrier Aggregation
Delay requirements for V2X CC addition/release based on dedicated RRC signaling.
  No need to introduce delay requirements for sidelink transmission mode 4
    It is left to UE implementation.
  FFS delay requirements for sidelink transmission mode 3
    The addition/release delay is just for the case of a single RRC addition/release command
    Companies are encouraged to provide the definition of V2X CC addition/release delay

## Slide 4: Agreements on V2X Carrier Aggregation
Interruption at V2X CC addition/release for V2X CA.
  Interruptions to WAN for the case V2X CC and WAN CC is not in the same band
    An interruption of up to 2 subframes is allowed.
    FFS the location of the interruption.
  Interruptions to V2X receptions/transmissions on other component carriers used for V2X CA
    No need to introduce interruption requirements for sidelink transmission mode 4
      It is left to UE implementation.
    FFS interruption requirements for sidelink transmission mode 3
      The interruption is investigated based on the assumption that AGC settling time for Rel-15 V2X is same as that for Rel-14 V2X
      Further study the location of the interruption