## Slide 1: Way forward on UE demodulation and CSI for FeCOMP
Intel Corporation, ZTE
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26 February – 2 March 2018
Agenda Item: 6.23.2
R4-1803108

## Slide 2: UE Demodulation Requirements
Test cases
  RAN4 84bis: Test #1: 2RX UE receives 2 MIMO layers PDSCH (1 MIMO layer per TP)
  RAN4 85: Test #2: 4RX UE, 3 MIMO layers PDSCH (2 MIMO layer from TP1 and 1 MIMO layer from TP2)
  Test #3: 4RX UE, 4 MIMO layers PDSCH (2 MIMO layer from TP1 and 2 MIMO layer from TP2)
Antenna configuration:
  RAN4 84bis: Test #1: 2x2 ULA low (for TP1-UE and TP2-UE links)
  RAN4 85: Test #2: 4x4 ULA low (for TP1-UE and TP2-UE links)
  Test #3: 4x4 ULA low (for TP1-UE and TP2-UE links)
Power imbalance
  RAN4 84bis: Test #1: Equal power between the TPs (SNRTP1 = SNRTP2)
  RAN4 85: Test #2: TP2 SNR is [3] dB lower than TP1 SNR (SNRTP1 = SNRTP2 + [3]dB)
  Test #3: Equal power between the TPs (SNRTP1 = SNRTP2)
FRC:
  RAN4 84bis: Test #1: 16QAM, 1/2, Rank 1 for each TP
  RAN4 85: Test #2:
    TP1: 16QAM, 1/2, Rank 2
    TP2: 16QAM, 1/2, Rank 1
  Test #3: 16QAM, 1/2, Rank 2 for each TP
Number of CRS APs:
  RAN4 84bis: Test #1: 2 CRS APs for each TP
  Tests #2: 2 CRS APs for each TP
  Tests #3: 4 CRS APs for each TP
Note: Previous agreements are marked as green

## Slide 3: CSI Reporting Requirements (1)
Antenna configuration: 2x2 ULA Low antenna correlation (for TP1-UE and TP2-UE links)
Test setup includes 2 TPs (serving TP1 and TP2)
  No time/frequency offset between the TPs
  Colliding CRS patterns with Different Cell IDs
      CSI reporting
  UE is configured with K = 2 NZP CSI-RS resources and one CSI-IM resource
  2 CSI-RS antenna ports are configured for each NZP CSI-RS resource
  ZP CSI-RS configurations are aligned among TPs
  Aperiodic CSI reporting
      Companies are encouraged to provide simulation results and view on CSI requirements options from slides 4-5.
  Downselection will be made in the next RAN4 meeting (RAN4 #86bis)

## Slide 4: CSI Reporting Requirements (2)
CSI reporting assumptions:
  Option 1:
    Fixed RI and CQI per TP (fixed reference channel): Rank 1, 16QAM, MCS 13
    Follow PMI and CRI
    Equal power between TPs
  Test purpose: Verify proper CRI reporting
  Test metrics:
    Use the following metrics:
    is [X] % of the maximum throughput obtained at SNRFollowCRI using the CRI configured according to the CSI UE report
    is the throughput obtained at SNRFollowCRI under assumption of single TP transmission (TP1 transmission)

## Slide 5: CSI Reporting Requirements (3)
CSI reporting assumptions:
  Option 2:
    Fixed RI and CQI per TP (fixed reference channel): Rank 1, 16QAM, MCS 13
    Follow PMI and CRI
    FFS power imbalance between TPs
  Test purpose: Verify proper CRI reporting
  Test metrics:
    Use the following metrics:
    is the throughput obtained at SNRFixedTP1 using the CRI configured according to the CSI UE report
    is [X] % of the maximum throughput obtained at SNRFixedTP1 under assumption of single TP transmission (TP1 transmission)
    FFS other details (how many test points needed, etc. )