## Slide 1: Way forward on higher velocity UE RRM requirements
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26th February – 2nd March, 2018
Agenda item: 6.19.4.1
R4-1803127

## Slide 2: Background
We have reached the following agreements in RAN4 #85:
  For non-DRX requirements with gap pattern #0 and for intra-frequency measurement
    Reuse Rel-13 cell identification and measurement delay requirements in high Doppler channel up to 220Hz Doppler spread.
    Reuse Rel-13/14 measurement accuracy requirements in high Doppler channel up to 220Hz Doppler spread.
  FFS for inter-frequency measurement requirements
  FFS for RRM requirements with DRX

## Slide 3: Way forward
DRX measurement requirements
  Under RRC_IDLE state
    TIdentify_Intra_UE cat M1 and Tmeasure_intra_UE cat M1 should be reduced due to faster UE velocity
    Gap sharing should be considered when consider values in the above table
DRX cycle length (s) | Tdetect_intra (s) (DRX cycles) | Tmeasure_intra (s) (DRX cycles) | Tevaluate_intra (s) (DRX cycles)
0.32 | [TBD] | [TBD] | [TBD]
0.64 | [TBD] | [TBD] | [TBD]
1.28 | [TBD] | [TBD] | [TBD]
2.56 | [TBD] | [TBD] | [TBD]

## Slide 4: Way forward
  Under RRC_CONNECTED state
    TIdentify_Intra_UE cat M1 and Tmeasure_intra_UE cat M1 should be reduced due to faster UE velocity
    Gap sharing should be considered when consider values in the above table
DRX cycle length (s) | Tidentify_intra (s) (DRX cycles) | Tmeasure_intra (s) (DRX cycles)
≤0.04 | [0.8] (Note1) | [0.2] (Note1)
[0.04<DRX-cycle≤0.08] | Note2([TBD]) | Note2 ([TBD])
[0.08<DRX-cycle≤1.28] | Note2([TBD]) | Note2 ([TBD])
[1.28<DRX-cycle≤2.56] | Note2([TBD]) | Note2 ([TBD])
Note1: Number of DRX cycle depends upon the DRX cycle in use. Note2: Time depends upon the DRX cycle in use. |  | 

## Slide 5: Way forward
  On gap sharing
    Introduce gap sharing table for eFeMTC UEs supporting higher velocity
  On informing higher velocity operation
    Indication for eFeMTC UEs that support higher velocity operation shall be used
    Higher velocity UE measurement requirements in DRX should apply when the above indication is signalled