## Slide 1: WF on 1 Rx CRS-IM performance requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26 February – 2 March 2018
Agenda Item: 6.23.2
R4-1803155

## Slide 2: Cat 1bis requirements
PDSCH test cases
  Test #1:
    TM4, 4 CRS APs, 24 PRBs, MIMO Rank 1
    FRC: 64QAM (MCS20)
    Interference loading: 20%
    Beamforming model: Follow PMI
  Test #2:
    TM9, 2 CRS APs, 24 PRBs, MIMO Rank 1
    FRC: QPSK (MCS9)
    Interference loading: 10%
    Beamforming model: Random PMI
PDCCH test cases
  Test #1: PDCCH AL4, 2 CRS APs, CFI = 1
  Test #2: PDCCH AL4, 4 CRS APs, CFI = 2
  TDD parameters
  UL/DL configuration 1
  Special subframe type 4
Note: Previous agreements are marked as green

## Slide 3: Cat M2 requirements
PDSCH test cases
  CE mode A
  Test #1:
    No repetitions and no frequency hopping
    TM6 with 4 CRS APs, MIMO Rank 1
    FRC: 16QAM (MCS14)
    Interference loading: 20%
  Test #2:
    No repetitions and frequency hopping is FFS
      Option 1: No frequency hopping
      Option 2: Frequency hopping with frequency hopping offset = 5 and frequency hopping interval = 4 ms
    TM6 with 2 CRS APs, MIMO Rank 1
    FRC: 16QAM (MCS14)
    Interference loading: 10%
MPDCCH test cases
  CE mode A
  No repetitions and no frequency hopping
  Test #1: MPDCCH AL4, 0% interference loading
  Test #2: MPDCCH AL16, 10% interference loading
  TDD parameters
  UL/DL configuration 1
  Special subframe type 4
Note: Previous agreements are marked as green

## Slide 4: UE Capabilities
Reuse legacy CRS-IM UE capability signalling to trigger CRS network assistance