## Slide 1: WF for NR FR1 PC2 MPR and PC3 A-MPR for UTRA ACLR
Nokia, Qualcomm, Skyworks
R4-1803252

## Slide 2: Proposals in RAN4#86 Athens
REFERENCES
[1] R4-1802240, Qualcomm
[2] R4-1802514, Skyworks
[3] R4-1802103, Nokia
Additional PC2 backoff compared to PC3 |  |  |  |  | 
outer | Modulation | PC3 MPR (dB) | Qualcomm | Nokia | Skyworks
 | DFT-s-OFDM PI/2 BPSK | ≤ 0.5 | 0 | 0 | 0
 | DFT-s-OFDM QPSK | ≤ 1 | 0 |  | 
 | DFT-s-OFDM 16 QAM | ≤ 2 | 0 |  | 
 | DFT-s-OFDM 64 QAM | ≤ 2.5 | 0 |  | 
 | DFT-s-OFDM 256 QAM | ≤ 4.5 | 0 |  | 
 | CP-OFDM QPSK | ≤ 3 | 0 |  | 
 | CP-OFDM 16 QAM | ≤ 3 | 0.5 |  | 
 | CP-OFDM 64 QAM | ≤ 3.5 | 0.5 |  | 
 | CP-OFDM 256 QAM | ≤ 6.5 | 0 |  | 
Inner | DFT-s-OFDM PI/2 BPSK | 0 | 0 |  | 
 | DFT-s-OFDM QPSK | 0 | 0.5 |  | 
 | DFT-s-OFDM 16 QAM | ≤ 1 | 0 |  | 
 | CP-OFDM QPSK | ≤ 1.5 | 0 |  | 
 | CP-OFDM 16 QAM | ≤ 2 | 0 |  | 

## Slide 3: Way forward for NR FR1 PC2 MPR
Agreement: NR FR1 PC3 MPR applies also for FR1 PC2 unless otherwise
Fundamental issues are founed.

## Slide 4: Proposals for UTRA ACLR A-MPR
R4-1802104 (Nokia) – No A-MPR is needed. The agreed MPR is sufficient.
R4-1802701 (Skyworks) –
  CP-OFDM, 16QAM, 5 MHz, full allocation marginal for UTRA1
  20 MHz full allocation, 10 MHz full allocation marginal for UTRA2
R4-1802238 (Qualcomm) – See table
Modulation | A-MPR (dB) | 
 | Outer RB allocations | Inner RB allocations
DFT-s-OFDM PI/2 BPSK | ≤ 1.5 | 0
DFT-s-OFDM QPSK | ≤ 1 | 0
DFT-s-OFDM 16 QAM | ≤ 0.5 | 0
DFT-s-OFDM 64 QAM | ≤ 0.5 | 
DFT-s-OFDM 256 QAM | ≤ 0.5 | 
CP-OFDM QPSK | ≤ 1 | 0
CP-OFDM 16 QAM | ≤ 1 | 0
CP-OFDM 64 QAM | ≤ 0.5 | 
CP-OFDM 256 QAM | ≤ 0.5 | 

## Slide 5: Way forward for A-MPR for UTRA ACLR
Agree to following table. A-MPR only for outer region
NS_02 (UTRA protection) can be signaled to bands at least 1,2,5 and 8. It is important to list the bands so that RAN5 know for which bands UTRA protection needs to be tested
Modulation | A-MPR (dB) | 
 | Outer RB allocations | Inner RB allocations
DFT-s-OFDM PI/2 BPSK | ≤ 1.5 | 0
DFT-s-OFDM QPSK | ≤ 1 | 0
DFT-s-OFDM 16 QAM | ≤ 0.5 | 0
DFT-s-OFDM 64 QAM | ≤ 0.5 | 0
DFT-s-OFDM 256 QAM | 0 | 0
CP-OFDM QPSK | ≤ 1 | 0
CP-OFDM 16 QAM | ≤ 1 | 0
CP-OFDM 64 QAM | ≤ 0.5 | 0
CP-OFDM 256 QAM | 0 | 0