## Slide 1: WF on MPR for FR2
Intel, Qualcomm
3GPP TSG-RAN WG4 Meeting #86 R4-1803263
Athens, Greece, 26 Feb - 2 Mar, 2018
Agenda Item: 7.4.9.5

## Slide 2: Background
Previous agreements:
The reference waveform and power class definition waveform assumptions from the Reno meeting[1]
  The waveform defined by BW = 100MHz, SCS=60KHz, DFT-S-OFDM QPSK, 128RB0 is the reference waveform with 0dB MPR and is used for the power class definition
DPD assumption on FR2 MPR from San Diego meeting [2]
  A single MPR table is defined for all UEs whether they support the PA calibration gap or not
  Assumption for MPR work is that UE applies calibration
FR2 MPR table format[3]
  For 50M/100M/200M assign a single MPR value relative to MPR 0 for each waveform and modulation
  For 400M, add MPR offset based on practical implementation
    Companies are encouraged to measure the effect large BW on MPR

## Slide 3: WF on MPR for FR2
Companies co-signing this contribution propose NR FR2 MPR as listed in WF column.
Note:
UE requirements for the waveform defined by BW = 100MHz, SCS=60KHz, DFT-S-OFDM Pi/2 BPSK, 128RB0 shall be set to [-2 to 0]dB MPR
Above WF MPR table is applicable to network supporting calibration gap assumed that UE is provided with PA calibration gap when UE needs

## Slide 4: Reference
[1] R4-1714445, “WF on pulse shaping and power class FR2”, Intel Corporation, Apple, Qualcomm, IITH, LGE, Nokia , Huawei, Motorola Mobility, 3GPP TSG-RAN WG4 Meeting #85,Reno, Nevada, USA
[2] R4-1801200, “WF on PA calibration gap parameters”, Qualcomm, Intel, 3GPP TSG-RAN WG4 AH meeting, San Diego, USA
[3] R4-1801192, “WF on mmW MPR”, Qualcomm, 3GPP TSG-RAN WG4 AH1801 Meeting San Diego, CA
[4] R4-1801774, “MPR evaluation results for FR2”, Intel, 3GPP TSG-RAN WG4 Meeting #86, Athens, Greece
[5] R4-1801639, “FR2 MPR”, Qualcomm, 3GPP TSG-RAN WG4 Meeting #86, Athens, Greece