## Slide 1: WF on FR2 SEM
Samsung,…
3GPP TSG-RAN WG4 RAN4 #86
Athens, Greece, Feb 6st-Mar 2nd, 2018
R4-1708867

## Slide 2: Background
In WF on FR2 SEM agreed in RAN4 NR AH#1702 [1] it states that :
    Following variations for the BS transmitter mask tables should be use:
      BS classes
      Power levels
      Frequency ranges
In WF on FR2 SEM agreed in RAN4#84 [2]
  The mask for Wide Area BS was agreed as below single table:
  The mask for Local Area and Medium Range BS was FFS
    The Ptx was addressed in title of Medium Range BS Mask table
Agreed TP on FR2 SEM in RAN4 NR AH#1703 in [3]
  BS class is removed in proposed TP.
In all agreed contributions mentioned above, the OOB boundary is considered should to be applied according to ITU-R SM.1539 recommendation.
The absolute ACLR is defined as below in TS38.104:
  Usually the absolute ACLR is relative stricter than unwanted emission for the range with the same measurement bandwidth.
Frequency offset from “edge of transmission” Δf | Emission limit | Measurement bandwidth
0  f < 10% of the total transmission bandwidth | -5 dBm | 1 MHz
10% of the total transmission bandwidth  f < OOB boundary | -13 dBm | 1 MHz
f ≥OOB boundary | Spurious domain limits | 1 MHz
BS class | ACLR absolute limit
Wide-area BS | -13 dBm/MHz
Medium-range BS | [-20 dBm/MHz]
Local-area BS | [-20 dBm/MHz]

## Slide 3: Way forward(1)
Issue 1: Mask type as SEM(carrier-centric/ contiguous transmission spectrum centric) or OBUEUEM(band-centric)
    Target to align the mask type for category A and category B in 3GPP NR specification as long as there is no confliction with each regional requirement and decide one of below options to proceed in RAN4#86bis
  Option 1: SEM (carrier centric or contiguous transmission spectrum centric) as current definition as Category A and FFS on Category B definition when it is available.
  Option 2: UEMOBUE (band centric) to accommodate foreseeable Category B emission requirement in EU to avoid potential very strict spurious emission requirement within the operating band, which is assumed can not be achieved without RF filter, to be applied within operating band, which is hard to handle.
Issue 2: OOB boundary which is dependent on decision of issue 1
  Boundary based on ITU-R recommendation SM.1539 as table below if SEM definition agreed
    FFS on definition of the contiguous allocated transmission bandwidth and its notation
  Such as whether it to be replaced by replaced by Base Station RF Bandwidth
  Boundary defined as below if UEM OBUE definition agreed
    Spectrum emission mask limits in FR2 are defined from ΔfOBUE below the lowest frequency of each supported downlink operating band up to ΔfOBUE above the highest frequency of each supported downlink operating band.
    FFS on ΔfOBUE taken into account the filter implementation when category B requirement is available.
Center frequency of the contiguous allocated transmission bandwidth fc | The contiguous allocated transmission bandwidth BWcontiguous | The maximum offset of spectrum emission mask from the contiguous allocated transmission bandwidth edge ΔfSEM
24.25GHz ≤ fc ≤ 56GHz | BWcontiguous < [500MHz] | 2*Bwcontiguous
 | [500MHz ]≤ BWcontiguous | BWcontiguous + [500MHz]

## Slide 4: Way forward(2)
Issue 3: whether emission mask level should be scaled to maintain the same TRP PSD assumption for wanted signal (around 12dBm/MHz)
  This is related to BS class or Ptx indicated Ptx definition which somehow can be addressed in issue 4.
Issue 4: whether BS class or Ptx should be considered.
  BS class: FFS on rationality to define WA BS mask by frequency agnostic and power level agnostic way same as FR1 and LTE as table below
  Power level Ptx: FFS on definition of Ptx and the appropriate power level for MR and LA BS.
    Regarding the definition of Ptx at least FFS on following aspects:
      Defined as rated TRP power as declaration or maximum TRP power according to measurement
      Defined as total TRP power for contiguous spectrum or TRP power for edge carrier or the maximum carrier TRP power among contiguous carriers
    Regarding FFS on the Ptx threshold for mask is selection following options could be considered for further study
      Ptx threshold and m Mask levels should to be defined with consideration of levels used by ITU-R in compatibility studies
      Ptx threshold should consider the implementation reality
Frequency offset from “edge of transmission” Δf | Limit | Measurement bandwidth
0  f < 10% of the total transmission bandwidth | -5 dBm | 1 MHz
10% of the total transmission bandwidth  f < OOB boundary | -13 dBm | 1 MHz
Table SEM applicable for WA BS
 | 24.24-33.4GH Frequency range | 37 – 52.6 GHz Frequency range | Rough antenna element size
Option 1 | 35dBm | 33dBm | >1000
Option 2 | 32dBm | 30dBm | ~500
Option 3 | 29dBm | 27dBm | ~256
Option 4 | 26dBm | 24dBm | ~128

## Slide 5: Reference
Agreed WF or TP in previous discussion in NR WI
  [1] R4-1706964 WF on BS transmitter mask for mmWave RAN4 NR AH-1702
  [2]R4-1708866 WF on BS unwanted emission for NR mmWave bands RAN4#84
  [3] R4-1710075 TP to TR 38.xxx: Spectrum emission mask (SEM) for FR2 RAN4 NR AH-1703
Contributions on FR2 SEM discussed in RAN4#86:
  [4]R4-1801575 Consideration on FR2 SEM
  [5] R4-1801576 Draft CR for 38.104: FR2 SEM
  [6] R4-1802039 Further discussion on FR2 SEM requirement
  [7] R4-1802150 BS Emission mask for FR2
  [8] R4-1802151 Draft CR for TS 38.104: BS Emission mask for FR2
  [9] R4-1802878 SEM for FR2 NR BS
  [10] R4-1802879 Draft CR for TS 38.104: OTA out-of-band emissions (3.1, 3.2, 9.7.1 and 9.7.4)
  [11] R4-1803028 BS spectrum mask for BS type 2-O
  [12] R4-1803029 Draft CR to TS 38.104 clause 9.7.4.3 OTA spectrum emission mask