## Slide 1: WF on Signal type for receiver requirements for NR BS
Ericsson
R4-1803298

## Slide 2: WF on signal type for RF requirements
Agreement: DFT-S-OFDM is used for the interferer waveform
Agreement: All interferer power levels for all requirements remain as agreed in 38.104

## Slide 3: Interferer frequency offsets
Interferer frequency offsets requirement by requirement:
  Adjacent channel selectivity
    Interferer is placed at the centre of the adjacent channel
    If the SU is lower, then the gap to the wanted channel will be slightly higher
      For the 5MHz adjacent channel interferer, the SU for DFT-S-OFDM is exactly the same as CP-OFDM
      For the 20MHz adjacent channel interferer, the SU for the DFT-S-OFDM is 100 PRB compared to 106 PRB for CP-OFDM -> interfer edge would be 3 PRB further away from RF bandwidth edge than CP-OFDM
      For the 50MHz adjacent channel interferer, the SU for the DFT-S-OFDM is 64 PRB compared to 66 PRB for CP-OFDM -> interfer edge would be 1 PRB further away from RF bandwidth edge than CP-OFDM
    Solution:
      For 5MHz, same frequency offset from wanted signal band edge to centre of adjacent channel
      For 20MHz, change frequency offset by –(12*15*3)=-540kHz
      For 50MHz (FR2) change frequency offset by –(12*60*1)=-720kHz

## Slide 4: Interferer frequency offsets
General blocking
  5MHz interferer no difference in spectral utilization
  20MHz interferer SU is 100 PRB instead of 106 PRB
  The general blocker is in the 2nd channel, far away from the wanted signal. The absolute power is of importance; the change in distance from band edge to interferer will not make a large difference
  Conclusion: Do not change interferer frequency offset for general blocking
Narrowband blocking
  The interferer offset of the single PRB is calculated based on the minimum distance of the single PRB from the band edge to the interferer
  No need to update frequency offset

## Slide 5: Interferer frequency offsets
Receiver intermodulation
  With the existing frequency offsets, the interferer IM product will still fall inside the wanted signal despite any slightly smaller SU
  Conclusion: No need to change the frequency offset
Narrowband receiver intermodulation
  The frequency offsets of the CW and single PRB can stay the same; they are not impacted by the SU for DFT-S-OFDM
In channel selectivity
  In channel; no frequency offset