## Slide 1: Way Forward on FR2 Power Control
MediaTek Inc., Intel, Ericsson, LGE
3GPP TSG-RAN WG4 #86 Meeting R4-183371
Athens, Greece, Feb. 26th – Mar. 2nd, 2018

## Slide 2: Background
FR2 UE power control has been discussed in this meeting [1-4].
Beam correspondence was assumed as the prerequisite to enable the open loop power control mechanism as has been defined for E-UTRA UEs.
The open loop power control is meant to compensate the path loss to achieve a target UL power level at base station receiver input, where the path loss is calculated within UE by,
  Path Loss = referenceSignalPower – higher layer filtered RSRP
Consensus on the principle of open loop power control requirement and verification approach was reached in this meeting.

## Slide 3: Agreements
FR2 open-loop control requirement shall be defined and verified.
The requirement is defined as a target EIRP power level at tester antenna based on a reference signal power level sent by the tester.
The open-loop power control requirement shall be met at any beam direction provided the UE has sufficient power headroom to support the required target power level.

## Slide 4: Way Forward (1)
Companies are encouraged to study and propose the open-loop power control requirement and test method.
  How to define the reference signal power level?
  How to define the target UL EIRP power level and tolerance?
  How to select beam direction for verification?
Companies are also encouraged to study if relative power control requirement is needed and the verification method.
  Number of control steps and tolerance?
  Can it be verified by open-loop power control test method or a separate test method with TPC commands is needed?

## Slide 5: Way Forward (2)
Companies are encouraged to study how the open-loop power control can be applied for FR2 UEs without beam correspondence capability, assuming beam correspondence is not a mandatory feature.
Companies are encouraged to study if open-loop power control verification can be coupled with beam correspondence verification.

## Slide 6: References
[1] R4-1801803, “Open loop TPC for FR2”, Intel
[2] R4-1801951, “Absolute power control tolerance for FR2”, Qualcomm Inc.
[3] R4-1802281, “Concern over FR2 UE open-loop power control”, MediaTek Inc.
[4] R4-1802357, “Verifying absolute power control accuracy for FR2”, Ericsson