## Slide 1: WF for NR BW Class
Nokia
R4-1803374

## Slide 2: Background
NR CA BW Class was discuessed in UE RF session in RAN4#86 [1][2][3][4] and [1] was selected as a basis for WF.
[1] R4-1802111, CA BW Class, Nokia, Nokia Shanghai Bell
[2] R4-1801797, CA BW class definition, Intel Corporation
[3] R4-1802020, Further Considerations on BCS in NR, ZTE Corporation
[4] R4-1802209, NR CA BW Class for mmWave, Verizon UK Ltd

## Slide 3: WF for NR BW Class
Proposal 1: Define FR1 CA BW Class as presented in Slide 4
Proposal 2: Define FR2 CA BW Class as presented in Slide 5
  FBG1 assumes 400 MHz CCs, FBG2 assumes 200 MHz CCs, FBG3 assumes 100 MHz CCs and FBG4 assumes usage of 50 MHz CCs.
Proposal 3: UE can indicate support up to a certain aggregated bandwidth in MHz that is less than the maximum aggregated BW of certain CA BW Class. UE must support all specified aggregated bandwidths that are smaller than the indicated aggregated bandwidth and are part of same BCS that was indicated. UE must support also all specified lower order CA configuration that have same BCS as the indicated one.
Proposal 4: BCS with same number (for-example BCS0) need to be aligned between lower and higher order fallback configuration

## Slide 4: CA BW Class for FR1
NR CA bandwidth class | Aggregated channel bandwidth | Number of contiguous CC
A | CBW =< max CHBW | 1
B | 20 MHz ≤ CBW ≤ 100 MHz | 2
C | 100 MHz < CBW ≤ 2 x max CHBW | 2
D | 200 MHz < CBW ≤ 3 x max CHBW | 3
E | 300 MHz < CBW ≤ 4 x max CHBW | 4
NOTE: max CHBW is maximum channel bandwidth supported among all bands in a release |  | 

## Slide 5: CA BW Class for FR2
NR CA bandwidth class | Aggregated channel bandwidth | number of contiguous CC | Fallback group
A | CBW ≤ 400 MHz | 1 | 
B | 400 MHz < CBW ≤ 800 MHz | 2 | 1
C | 800 MHz < CBW ≤ 1200 MHz | 3 | 
D | 200 MHz < CBW ≤ 400 MHz | 2 | 2
E | 400 MHz < CBW ≤ 600 MHz | 3 | 
F | 600 MHz < CBW ≤ 800 MHz | 4 | 
G | 100 MHz < CBW ≤ 200 MHz | 2 | 3
H | 200 MHz < CBW ≤ 300 MHz | 3 | 
I | 300 MHz < CBW ≤ 400 MHz | 4 | 
J | 400 MHz < CBW ≤ 500 MHz | 5 | 
K | 500 MHz < CBW ≤ 600 MHz | 6 | 
L | 600 MHz < CBW ≤ 700 MHz | 7 | 
M | 700 MHz < CBW ≤ 800 MHz | 8 | 
O | 100 MHz ≤ CBW ≤ 400 MHz | 2 | 4
P | 150 MHz ≤ CBW ≤ 400 MHz | 3 | 
Q | 200 MHz ≤ CBW ≤ 400 MHz | 4 |