## Slide 1: WF on the test methodology of beam correspondence
LG Electronics, Media Tek
3GPP TSG-RAN WG4 #86 Meeting Athens, Greece, 26 - 02 Febrauary 2018 Agenda Item: 7.4.9.12
R4-1803458

## Slide 2: Background
RAN4 discussed how to define the beam correspondence RF requirements in TS38.101-2.
Three companies provided the detail test methodology as below
  [1] LGE (R4-1801637): EIS based EIRP beam correspondence evaluation
  [2] Media Tek (R4-1802282) : Partial & full beam correspondence evaluation
  [3] Qualcomm (R4-1800731) : Real Tx and best Tx beam correspondence evaluation
During online/offline discussions, companies discussed pros and cons according to the proposed test methodologies.
One remaining issue for EIS requirements is whether to define the CDF based EIS requirements or not.
The CDF based EIS for spherical coverage is quite similar to that with EIRP if the beam reciprocity between Rx beam and Tx beam is guaranteed.
This WF is on the related discussions on how to specify the beam correspondence test methodology and exception of CDF based EIS spherical coverage for beam correspondence capable UE.

## Slide 3: Definition
Beam correspondence:
  UE aspects in RAN1:
    UE is able to determine a UE Tx beam for the uplink transmission based on UE’s downlink measurement on UE’s one or more Rx beams.
    UE is able to determine a UE Rx beam for the downlink reception based on TRP’s indication based on uplink measurement on UE’s one or more Tx beams.

## Slide 4: Summary of comparison
Test method | Pros | Cons
[1] by LGE | - Evaluate difference of direction and power between Tx and Rx beam | - Not simple test compare with QC proposal - Need to know UE ant. Configuration and a lot of antennas. - Difficult to decide the distance between antennas
[2] by MTK | - UE implicitly verify by using the spherical coverage test | - Can not differentiate “full” and “partial” beam correspondence -New concept for “partial” beam correspondence and too late to introduce in rel-15 - Adjacent UE can be impacted by unmatched direction between Tx and Rx beam
[3] by QC | - Simple test for power difference between Tx and Rx beam | - No EIRP CDF test time saving for UEs with beam correspondence capability as beam sweeping is always required. - Adjacent UE can be impacted by unmatched direction between Tx and Rx beam

## Slide 5: Way Forward
The metric to choose the test methodology for beam correspondence RF requirement is test simplicity to save the OTA test time.
  RAN4 will specify the minimum RF requirements of beam correspondence based on [2] to reduce the test time and test burden and inform to RAN WG5 for the test methodology of beam correspondence.
  FFS how to capture the full beam correspondence RF requirements.