## Slide 1: WF on RLM requirements for NR
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86
Athens, Greece, Feb 26th- Mar 2nd, 2018
R4-1803477
Document for: Approval

## Slide 2: WF on hypothetical PDCCH
DCI format 1-0 is used for out-of-sync evaluation.
Companies are encouraged to provide simulation results based on R4-1801068 with further clarifications
  Practical Receiver (practical CE/NE and practical decoder)
  Interleaver size (R) = 3
  Interleaver nshift = 0
  Payload size for DCI format 1-0: 56/58/60 for 24/48/96 PRBs BW
  Payload size for DCI format 1-1: 90/92/94 for 24/48/96 PRBs BW
RAN4 to decide the hypothetical PDCCH parameters considering at least following
  Absolute Qout and Qin levels: should be compared to LTE, e.g. difference is <2dB
  Gap between Qin and Qout: should be based on SINR accuracy, e.g. >5dB
RAN4 to further discuss the need for adjusting the following PDCCH parameters to achieve reasonable Qout and Qin levels
  DCI format
  Power boosting for on PDCCH data and DMRS Res
  Aggregation Level

## Slide 3: WF on requirements for FR2
FFS whether RLM causes interruption (similar as intra-frequency measurement) or not
FFS whether Rx beam sweeping factor is applied for RLM
RAN4 to further discuss the following scenarios for RLM regarding the timing relationship between RLM-RS and intra-frequency SMTC:
  Fully non-overlapping (not applicable for SSB)
    None of RLM-RS occasions is within SMTC
    RLM is performed in all available RLM-RS resources
  Partially overlapping
    Some but not all RLM-RS occasions is within SMTC
      RLM is performed in available RLM-RS resources outside SMTC
      FFS whether RLM is also performed in available RLM-RS resources within SMTC
  Fully overlapping
    All RLM-RS occasions are within SMTC
    FFS whether requirements are defined for this configuration
    RLM is performed in available RLM-RS resources within SMTC
  In case requirements are defined for RLM performed in available RLM-RS resource within SMTC, time sharing between RLM and intra-frequency measurement is FFS

## Slide 4: WF on DRX requirements
Scaled by [1.5] for short DRX cycle, no scaling for long DRX cycles. The boundary for short and long DRX cycle is TBD
FFS whether scaling for L1 indication period should be applied or not

## Slide 5: WF on CSI-RS requirements
Evaluation period
  Companies are encouraged to provide simulation results based on R4-1801301, to conclude on the RLM requirements
Hypothetical PDCCH parameters
  FFS

## Slide 6: WF on link reconfiguration
Companies are encouraged to provide opinions on whether RRM requirements for link reconfiguration should be defined
  Link reconfiguration procedure is defined in section 6 of 38.213

## Slide 7: Other open issues
Whether the same PDCCH parameters are used for any SCS of the RLM-RS being measured