## Slide 1: Way forward on eFeMTC RRM requirements for CRS muting
Ericsson, [Huawei, HiSilicon, Nokia, Nokia Shanghai Bell, Qualcomm Incorporated]
3GPP TSG-RAN WG4 Meeting #86 R4-1803488
Athens, Greece, 26 February – 2 Mars, 2018
Agenda Item: 6.19.4.2

## Slide 2: Proposals for CRS muting
Initial cell acquisition
  when UE has EARFCN pre-provisioning
    UE may assume that there is no full BW CRS transmission
  when UE does not have EARFCN pre-provisioning
    full BW CRS is transmitted in 1 DL subframe every 20 ms.
Muted CRS BW for category M2
  Baseline: CRS transmissions over central 6 PRBs within serving cell BW
    Category M1 transmit timing error requirements of 24*Ts applies for category M2
  If CRS transmissions over central 24 PRBs within serving cell BW are used, network shall indicate this to the UE.
    If this indication is received, category M2 transmit timing error is defined as 12*Ts