## Slide 1: Draft WF on Feasibility of two NTA offset for FR2
Qualcomm

## Slide 2: Motivation
Assuming 2 symbol PDCCH and 2 symbol DMRS
  Each extra symbol used for switching between Rx and Tx is 10% throughput hit per slot
Forward compatibility
  Without signaling, legacy UE’s in network will prevent a change in TA offset value in future
  This would prevent 1 symbol switching from being ever implemented for 120KHz SCS

## Slide 3: TA offset impact on Rx to Tx switching time
TA offset impacts number of symbols needed for Rx to Tx switch at UE
For UE max available time for Rx to Tx switch if total switch needs to be done in n symbols
  TRXTX = n*Tsym – TA – TAoffset
0
1
2
3
4
11
12
13
BS Timeline
0
1
TAoffset
Slot
0
1
2
3
4
11
12
13
UE Timeline
0
1
Tprop
Tprop
Tprop+TA offset
2
2
TRXTX
TTXRX

## Slide 4: 1-symbol switching in 120KHz SCS
Current TA offset for FR2 – 13763 Tc = 7us
For a UE that is 300 mts away from gNodeB TA = 2 us
TA_offset + TA = 7+2 > 8.92 = Tsym
  1 symbol switching is not feasible
Even with no TA, the max TRxTx = 8.92 – 7 = 1.92 which is infeasible for UE

## Slide 5: Proposals for Investigation
Proposal 1: Companies to investigate whether it is feasible from both UE and network perspectives to have two values of NTA_offset for FR2: existing value (13763 Tc) in TS 38.133 and a shorter value. The shorter value is FFS.
  Companies to also investigate the system performance benefit
Proposal 2: If based on RAN4 studies, two NTA_offset values are considered to be feasible, then RAN4 will request RAN2 to introduce 1-bit broadcast signaling in FR2 for UE to know which TA offset to use. The larger NTA offset value can be used as default
Interested companies are to provide their views including the feasible value of the second NTA_offset (shorter value) for FR2