## Slide 1: WF on FR2 receiver spurious emissions requirement
NTT DOCOMO, INC., Nokia, Huawei
3GPP TSG-RAN Working Group 4 (Radio) meeting #86 R4-1803530
Athens, Greece, 26th February - 2rd March, 2018
7.6.3.5.2 OTA receiver spurious emissions [NR_newRAT-Core]

## Slide 2: Background
The receiver spurious requirement for FR2 was agreed in RAN4 #85 [1].
However, the issue that the receiver spurious emissions limit (-47dBm/MHz) are lower than transceiver OFF power limits (-36dBm/MHz) was obtained in [2], and WF was agreed [3].
In RAN4 #86, this open issue is discussed [4-8].
Reference:
  [1] R4-1714433, TP to TS 38.104: OTA Rx spurious emissions for BS type O 2 (10.7.3), Huawei
  [2] R4-1800756, Discussion on FR2 Rx emissions, Huawei
  [3] R4-1801281, WF on FR2 Rx spurious emissions, NTT DOCOMO, INC
  [4] R4-1802877, Receiver spurious emissions for FR2 NR BS, NTT DOCOMO, INC.
  [5] R4-1802976, FR2 RX spurious emissions, Huawei
  [6] R4-1802152, Receiver spurious emission FR2, Ericson
  [7] R4-1802153, Draft CR for TS 38.104: Receiver spurious emission FR2, Ericsson
  [8] R4-1802741, Draft CR on OTA receiver spurious emissions requirement (10.7)

## Slide 3: Discussion
The applied frequency ranges are different between the transmitter OFF power (In-band) and the receiver spurious emissions (out-of-band) [4].
The measurement frequency ranges are overlapping between BS type 1-O and 2-O [4].
In transceiver spurious emission requirement, the testability does not affect the core requirement (frequency upper limit will be changed from core requirement) [4].
Existing requirements for E-UTRA/UTRA co-location and co-existence requirements are already the same between Tx and Rx [5].
The current FR2 Rx emissions level is higher than the TX OFF requirement [5].
For TDD out of band emissions it makes no sense to have different Tx and Rx requirements [5].
The existing RX emissions limit is difficult to measure OTA [5].
During the transmitter ON period, it is assumed that other similar services on the same (and nearby frequencies) are in transmit mode and are not impacted by strong interference from the transmitter. This is thoroughly analyzed through 3GPP co-ex studies, resulting in ACLR and ACS requirements. Other services further away in frequency are protected by the Transmitter spurious emission limits (clause 9.7.5 of TS 38.104) [6].
During transmitter OFF, it is assumed that similar services are in receive mode and a Transmitter OFF power requirement provides protection for those [7].

## Slide 4: Discussion
The company’s views are summarized in below Table 1.
 | NTT DOCOMO R4-1802877 [4] | Huawei R4-1802976 [5] | Ericsson R4-1802152 [6] R4-1802153 [7] | Compromise
30MHz-1GHz | -57dBm/100kHz | -57dBm/100kHz | -36dBm/100kHz | -57dBm/100kHz
1GHz-12.75GHz | -47dBm/1MHz | -47dBm/1MHz | -36dBm/1MHz | -47dBm/1MHz
12.75GHz-2nd harmonic of the upper frequency edge of the UL operating band | -47dBm/1MHz | -36dBm/1MHz | -36dBm/1MHz | -36dBm/1MHz
Table 1: Summary of views for receiver spurious emission limits for BS type 2-O

## Slide 5: Agreement
Spilt the receiver spurious emission frequency range between frequencies covered by FR1 and those unique to FR2.
The FR2 (above 12.75GHz) emissions level should be based on the transceiver OFF level (-36dBm/MHz).
Above agreements are captured in draft CR [8]
Testability issues for OTA measurement are remained and will be discussed in conformance parts.
Frequency range | Limit | Measurement bandwidth | Note
30 MHz – 1 GHz | -57 dBm | 100 kHz | Note 1
1 GHz – 12.75GHz | -47 dBm | 1 MHz | Note 1
12.75GHz - 2nd harmonic of the upper frequency edge of the UL operating band | -36 dBm | 1 MHz | Note 1, Note 2
NOTE 1: Bandwidth as in ITU-R SM.329 [3], s4.1 NOTE 2: Upper frequency as in ITU-R SM.329 [3], s2.5 table 1. NOTE 3: The frequency range between 2.5 * BWChannel below the first carrier frequency and 2.5 * BWChannel above the last carrier frequency transmitted by the BS, where BWChannel is the BS channel bandwidth according to subclause 5.3, may be excluded from the requirement. However, frequencies that are more than ΔfOBUE below the lowest frequency of the BS transmitter operating band or more than ΔfOBUE above the highest frequency of the BS transmitter operating band shall not be excluded from the requirement. |  |  | 
Table 10.7.3-1: Radiated Rx spurious emission limits for BS type 2-O