## Slide 1: Way forward on Scell activation delay
Intel, [], …
R4-1804187
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, AU, 16th – 20th April, 2018
Agenda Item: 7.9.10.3

## Slide 2: SCell activation delay
Background: it was agreed in RAN4#86 that
  Tactivation_time is consisted of
    RF warm up excluding AGC settling: TBD and independent of SCS
    AGC settling: N1(*) SMTC periods for known and N2 SMTC periods for unknown cells
    PSS/SSS and SSB index acquiring:
      X1 SMTC periods for known cell provided that PSS/SSS detection and MIB reading are not needed
      X2 SMTC period for known cell provided that MIB reading is needed
      X3 SMTC period for unknown cell provided that PSS/SSS detection and MIB reading are needed
      X1, X2 and X3 will be decided by RAN4#86bis

## Slide 3: Proposal
Proposal 1: Tactivation_time which is consisted of
    RF warm up excluding AGC settling: TBD and independent of SCS
    AGC settling: N1(*) SMTC periods for known and N2 SMTC periods for unknown cells
    PSS/SSS and SSB index acquiring:
can be specified as:
Tactivation_time | SCell unknown | SCell known with MIB reading | SCell known
FR1 | 0.5ms + [2+1+2]*SMTC_period | 0.5ms + [1+2]*SMTC_period | 0.5ms + [2]*SMTC_period
FR2 | 0.5ms + [2*N+2*N+2]*SMTC_period | 0.5ms + [2*N+2]*SMTC_period | 0.5ms + [2]*SMTC_period
It is noted that N can be less than the maximum TX beams numbers.
Proposal 2: The time for correct activation validation shall be counted into the overall Tactivation_time, e.g. CQI or RSRP measurement delay.