## Slide 1: WF on measurement gaps for dense PRS
Ericsson
3GPP TSG-RAN WG4 Meeting #86bis R4-1804697
Melbourne, Australia, 16th - 20th April, 2018
Agenda Item: 6.18.4.4

## Slide 2: Proposals
The existing UE Cat M1 and Cat M2 accuracy requirements for RSTD measurements in gaps shall also apply with the new gaps
The existing UE Cat M1 and Cat M2 measurement period requirements (generically formulated with respect to MGL and MGRP) for RSTD measurements in gaps shall also apply with the new gaps
The applicable measurement gap patterns need to be clarified in the RSTD requirements
Observations:
  Unlike in legacy case where only one measurement gap pattern (#0) was used for RSTD and the UE could therefore indicate only the offset and the frequency for which RSTD measurements are to be performed, with the introduction of the new gaps the UE should have a possibility to also indicate the preferred measurement gap pattern (corresponding to their MGL and MGRP specified in 36.133) including the new ones
  Legacy measurement gap pattern #0 can be used for RRM and RSTD
  The new measurement gap patterns may not be suitable for inter-frequency or inter-RAT RRM measurements
The new measurement gaps can be configured only for UE performing RSTD measurements requiring such gaps and shall be stopped upon completing these measurements
Option 1b is considered, while capturing in TS 36.133 the impact on RRM requirements during the RSTD measurement period
The existing RLM requirements for UE Cat M1 and Cat M2 can be met, provided there is no overlap between the new measurement gaps and MPDCCH subframes configured for UE monitoring

## Slide 3: Proposals (cont.)
New measurement gaps:
Gap Pattern Id | MGL (ms) | MGRP (ms) | Applicability
rstd0 | 6 | 40 | Only for CE Mode A
rstd1 | 10 | 80 | 
rstd2 | 10 | 160 | 
rstd3 | 10 | 320 | 
rstd4 | 10 | 640 | 
rstd5 | 10 | 1280 | 
rstd6 | 14 | 160 | 
rstd7 | 14 | 320 | 
rstd8 | 14 | 640 | 
rstd9 | 14 | 1280 | 
rstd10 | 32 | 320 | Only for CE Mode B
rstd11 | 32 | 640 | Only for CE Mode B
rstd12 | 32 | 1280 | Only for CE Mode B
rstd13 | 54 | 640 | Only for TDD with CE Mode B
rstd14 | 54 | 1280 | Only for TDD with CE Mode B
rstd15 | 64 | 640 | Only for measuring a cell based on two PRS configurations
rstd16 | 64 | 1280 | Only for measuring a cell based on two PRS configurations
rstd17 | 80 | 640 | Only for measuring a cell based on three PRS configurations
rstd18 | 80 | 1280 | Only for measuring a cell based on three PRS configurations
NOTE 1: Gap patterns rstd0-rstd18 can only be used during the corresponding RSTD measurement period and only for measuring on the carrier frequencies for which the UE is configured via LPP [24] to perform RSTD measurements requiring gaps. |  |  |