## Slide 1: WF on network-based CRS interference mitigation
Ericsson
3GPP TSG-RAN WG4 Meeting #86bis R4-1804701
Melbourne, Australia, 16th - 20th April, 2018
Agenda Item: 6.27.2

## Slide 2: Background
AllowedMeasBandwidth can be used to prevent UEs measuring over a large BW in intra-frequency and inter-frequency neighbor cells
  Earlier agreed (R4-1709102):
    If the UE is configured with widebandRSRQ-Meas to measure WB-RSRQ then the UE shall assume that CRS are available in the measured cell over the AllowedMeasBandwidth (e.g., 50 RBs or larger),
    Otherwise CRS may be transmitted over 6 RBs in neighbor cells (AllowedMeasBandwidth is 6 RBs)

## Slide 3: Signalling Support
SI and RRC signaling is used by the network to make the UE aware of whether network-based CRS interference mitigation is enabled or not
  The following information is needed for UE in RRC_CONNECTED and RRC_IDLE and is provided in SIB:
    Network-based CRS interference mitigation is enabled or disabled in the current cell, i.e., the cell transmitting the SIB
    For UE connecting to the network, this information should be possible to provide to the UE as early as possible
  The dedicated RRC signaling (e.g., neighCellsCRS-Info and neighCellsCRS-InfoSCell in TS 36.331) is enhanced to include an indication whether the network-based CRS interference mitigation is enabled or not in the serving cell(s), including PSCell and SCells, and one or more neighbor cells
  If the network-based CRS interference mitigation is not enabled in a cell, the network will transmit full bandwidth CRS, otherwise full-bandwidth CRS is guaranteed in the subframes of relevant cells as described in 36.133 (including warm-up and cool-down subframes) and 6RB CRS is guaranteed in the other subframes
  UE receiving the signaling can adapt its RRM/RLM procedures and interference mitigation schemes based on the received indications
UE choice indication of one of the two pre-defined warm-up/cool-down configurations
Send an LS to inform RAN2 about RAN4 agreements in this WF

## Slide 4: RAN4 Requirements
RAN4 will specify applicable requirements for Rel-15 UEs receiving the higher-layer signaling and define the corresponding warm-up/cool-down subframes in TS 36.133 for RRC_IDLE and RRC_CONNECTED (for different UE procedures in relevant subframes)
  Up to two warm-up/cool-down schemes can be specified
For UE not capable of receiving the aforementioned signaling a note in TS 36.300 is added that RRM and demodulation performance degradation may be possible for some UE