## Slide 1: Way forward on the performance part requirement side conditions
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 7.10.1
R4-1804753

## Slide 2: Background
The difference between NR and LTE in defining the side conditions for measurement accuracy requirements is that in NR the REFSENS is not only band agnostic but also depends on the subcarrier spacing used.
The reason for this is that when configured with different SCS, the bandwidth of the resource blocks are slightly different resulting in the slightly difference in REFSENS.

## Slide 3: Way forward
Define band groups with regard to the REFSENS of the NR operating bands and reuse the LTE band group table as the baseline.
when defining performance part requirements for NR, use per-RE minimum Io levels with the SCS scaling.
when defining side conditions in test cases for NR, use per-RE minimum Io levels with the SCS scaling either.

## Slide 4: Annex: band groups for NR
 | Group | NR FDD |  | NR TDD |  | 
 |  | Band group notation | Operating bands | Band group notation | Operating bands | 
 | A | NRFDD_A |  | NRTDD_A |  | 
 | B | NRFDD_B | n1 | NRTDD_B | n38, n50, n51, n70 | 
 | C | NRFDD_C | n66, n74 | NRTDD_C |  | 
 | D | NRFDD_D |  | NRTDD_D | n77, n78, n79 | 
 | E | NRFDD_E |  | NRTDD_E | n77 (3.8 to 4.2 GHz) | 
 | F | NRFDD_F | [n2], [n5], n7 | NRTDD_F | n41 | 
 | G | NRFDD_G | [n3], [n8], [n28] | NRTDD_G |  | 
 | H | NRFDD_H | [n20] | NRTDD_H |  | 
 | I | NRFDD_I |  | NRTDD_I |  | 
 | J | NRFDD_J |  | NRTDD_J |  | 
 | K | NRFDD_K | n71 | NRTDD_K |  | 
 | L | NRFDD_L |  | NRTDD_L |  | 
NOTE 1: The bands within the same group have the same Io conditions in a corresponding requirement in this specification. [Editor’s note: This table is to be updated with further confirmation of REFSENS of NR bands.] |  |  |  |  |  |